WHEC 2012 Abstract L.BECKERS

Abstract Title:

Investigating the factors for fermentative biohydrogen improvement: original bioreactors design and hydrogen partial pressure effect

| Submitting Author*: | BECKERS Laurent |
| --- | --- |

| Presenting Author*: | BECKERS Laurent |
| --- | --- |

| Affiliation: | CWB – University of Liège, Bld du Rectorat 29-B40, B4000 Liège, BELGIUM |
| --- | --- |

* Please note that you will be asked to enter all authors in the online form when uploading this abstract.

Abstract (maximum 200 words, Times New Roman, 12pt):

References (maximum 50 words):

[1] Das, D., International Journal of Hydrogen Energy, 34(17), 7349-7357, (2009) [2] Masset, J., International Journal of Hydrogen Energy, 35(8), 3371-3378, (2010) [3] Kraemer, J.T., International Journal of Hydrogen Energy, 33(22), 6558-6565, (2008) [4] Mizuno, O., Bioresource Technology, 73(1); 59-65, (2000)

# Text boxes

The anaerobic production of hydrogen from biomass offers the potential production of usable biogas from a variety of renewable resources. However, in order to produce hydrogen at high yields and production rates the biotechnological process needs to be further optimized and efficient bioreactors must be designed [1]. At the CWBI, a continuous horizontal rotating cylinder bioreactor has been designed and investigated to produce biohydrogen from glucose by the strain Clostridium butyricum [2] at good yields (1,9molH2·molglucose-1) and production rates (48,6mmolH2·Lmilieu-1.molhexose-1·h-1). This reactor has an internal volume of 2.3L and a small working volume (300ml) (fig.1).

It enhances the hydrogen production rates (by about three times more than a completely stirred bioreactor) by partially immobilizing the bacteria on the porous support. Moreover, the rotating cylinder design enables efficient H2 gas transfer from the liquid phase increasing hydrogen yields by about 25% compared to a completely stirred bioreactor [3-4]. Other original bioreactors, such as a trickle bed, have been built with the same aim of lowering the hydrogen partial pressure and led to similar results. Our work shows the importance of a good liquid to gas transfers in the biohydrogen-producing reactors to reach higher performances.

Fig.1: horizontal rotating cylinder bioreactor