“Stability of templated and nanoparticles dye-sensitized solar cells : photovoltaic and electrochemical investigation of degradation mechanisms at the photoelectrode interface”

Jennifer Dewalque et al.

Highly porous templated TiO2 films are promising alternative to nanoparticle layers for dye-sensitized solar cell applications. However, the increase of the electron transfer surface could promote detrimental side reactions and accelerate cell degradation upon ageing. Therefore, stability of templated cells under UV exposure, visible light soaking and thermal stress was studied in comparison to nanoparticle cells.