## Slide 1
New insights for an old topic: seagrasses as bioindicators
of coastal trace element
pollution.
J. Richir, P. Lejeune and
S. Gobert
Olhão, Portugal
03-2014

## Slide 2
bioindicators =
organisms accumulating pollutants to levels representative of their habitat pollution status
P. oceanica
direct measurements in the environment
trace elements
Mediterranean anthropic pressures
I
N
T
R
O
D
U
C
T
I
O
N
pollution
Introduction

## Slide 4
1
11
I
VII
P. oceanica sampled in 18 sites at 15 m depth in April 2007
19 TEs analysed by DRC-ICP-MS: Be, Al, V, Cr, Mn, Fe, Co, Ni, Cu, Zn, As, Se, Mo, Ag, Cd, Sn, Sb, Pb, Bi

## Slide 5
COASTAL
POLLUT
ION
e.g. 1 - V pollution

## Slide 6
newsvine.com
aria.developpement-durable.gouv.fr
corsematin.com
e.g. 1 - V pollution
COASTAL
POLLUT
ION

## Slide 7
newsvine.com
aria.developpement-durable.gouv.fr
corsematin.com
e.g. 1 - V pollution
Marseille oil refinery
Antibes oil-exporting harbour
Taglio-Isolaccio petroleum depot
COASTAL
POLLUT
ION

## Slide 8
e.g. 1 - Sb pollution
COASTAL
POLLUT
ION

## Slide 9
e.g. 1 - Sb pollution
COASTAL
POLLUT
ION

## Slide 10
2 – mining (Sb, Zn) / industrial (As) activities
Culioli et al. (2009)
e.g. 1 - Sb pollution
V

## Slide 11
COASTAL
POLLUT
ION
V vs. Sb

## Slide 14
How to order and to compare TEs according to the overall spatial variability of their environmental levels through the whole of a studied area ?

## Slide 15
How to order and to compare TEs according to the overall spatial variability of their environmental levels through the whole of a studied area ?
How to compare global pollution levels in TEs between several monitored sites ?

## Slide 16
How to order and to compare TEs according to the overall spatial variability of their environmental levels through the whole of a studied area ?
Trace Element Spatial Variation Index (TESVI)
TESVI = [(xmax/xmin) / (∑(xmax/xi)/n)] * SD
Trace Element Spatial Variation Index
TESV
I

## Slide 17
How to order and to compare TEs according to the overall spatial variability of their environmental levels through the whole of a studied area ?
Trace Element Spatial Variation Index (TESVI)
where:
xmax and xmin are the maximum and minimum mean concentrations recorded among the n sites,
xi are mean concentrations recorded in each of the n sites,
SD is the standard deviation of the weighted sum ∑(xmax/xi)/n.
The highest the index value, the more environmental levels of a TE globally vary (punctual contaminations and overall coastal spatial heterogeneity of TE levels taken into account) through the whole of the studied area the index is applied to.
TESVI = [(xmax/xmin) / (∑(xmax/xi)/n)] * SD
Trace Element Spatial Variation Index
TESV
I

## Slide 18
Trace Element Spatial Variation Index (TESVI)
TESVI = [(xmax/xmin) / (∑(xmax/xi)/n)] * SD
TESVI value calculation
TESV
I

## Slide 19
Trace Element Spatial Variation Index (TESVI)
TESVI = [(xmax/xmin) / (∑(xmax/xi)/n)] * SD
xmax/xmin
TESVI value calculation
TESV
I

## Slide 20
Trace Element Spatial Variation Index (TESVI)
TESVI = [(xmax/xmin) / (∑(xmax/xi)/n)] * SD
xmax/xmin
…
∑(xmax/xi)
SD
TESVI value calculation
TESV
I

## Slide 21
Trace Element Spatial Variation Index (TESVI)
TESVI = [(xmax/xmin) / (∑(xmax/xi)/n)] * SD
xmax/xmin
…
∑(xmax/xi)
SD
n
TESVI value calculation
TESV
I

## Slide 22
TESV
I

## Slide 23
TESVI values were listed in ascending order :
Se, Ni, Mn, Co, Sb, Ag, Be, Cu, Cd, Fe, Pb, Cr, Sn, As, Al, Zn, Bi, Mo, V
TESV
I

## Slide 24
TESVI values were listed in ascending order :
Se, Ni, Mn, Co, Sb, Ag, Be, Cu, Cd, Fe, Pb, Cr, Sn, As, Al, Zn, Bi, Mo, V
TESVI graphical representation

## Slide 25
TESVI values were listed in ascending order :
Se, Ni, Mn, Co, Sb, Ag, Be, Cu, Cd, Fe, Pb, Cr, Sn, As, Al, Zn, Bi, Mo, V
* highest xmax/xmin value
* highest xmax/xmin value
* highest xmax/xmin value
* highest xmax/xmin value
TESVI graphical representation

## Slide 26
TESVI values were listed in ascending order :
Se, Ni, Mn, Co, Sb, Ag, Be, Cu, Cd, Fe, Pb, Cr, Sn, As, Al, Zn, Bi, Mo, V
22.8
TESV
I

## Slide 27
TESVI values were listed in ascending order :
Se, Ni, Mn, Co, Sb, Ag, Be, Cu, Cd, Fe, Pb, Cr, Sn, As, Al, Zn, Bi, Mo, V
TESVI graphical representation

## Slide 29
How to compare global pollution levels in TEs between several monitored sites ?
Trace Element Pollution Index (TEPI)
TEPI = (Cf1 * Cf2 … Cfn)1/n,
Trace Element Pollution Index
TEP
I

## Slide 30
How to compare global pollution levels in TEs between several monitored sites ?
Trace Element Pollution Index (TEPI)
where:
Cfn is the mean normalized concentration of the TE n in a given monitored site.
The highest the index value, the more the monitored site is globally contaminated in TEs compared to the others.
TEPI = (Cf1 * Cf2 … Cfn)1/n,
a weighted version of the Metal Pollution Index (MPI) of Usero et al. (1996, MPB)
Trace Element Pollution Index
TEP
I

## Slide 31
Mean normalization
TEP
I

## Slide 32
Random list 1:
Be, Al, V, Cr, Mn, Fe, Co, Ni, Cu, Zn, As, Se, Mo, Ag, Cd, Sn, Sb, Pb, Bi
Random list 5:
Sb, V, Sn, Se, Be, Pb, Ni, Mo, Mn, Fe, Cu, Cr, Co, Cd, Bi, Zn, As, Ag, Al
Mean normalization

## Slide 33
Random list 1:
Be, Al, V, Cr, Mn, Fe, Co, Ni, Cu, Zn, As, Se, Mo, Ag, Cd, Sn, Sb, Pb, Bi
Random list 5:
Sb, V, Sn, Se, Be, Pb, Ni, Mo, Mn, Fe, Cu, Cr, Co, Cd, Bi, Zn, As, Ag, Al
Mean normalization

## Slide 34
TEPI for the French Mediterranean littoral
TEP
I

## Slide 35
TEP
I
TEPI for the French Mediterranean littoral

## Slide 37
P. oceanica

## Slide 38
P. oceanica

## Slide 39
P. oceanica

## Slide 40
Conclusion
Trace Element Spatial Variation Index
TESVI = [(xmax/xmin) / (∑(xmax/xi)/n)] * SD
Trace Element Pollution Index
TEPI = (Cf1 * Cf2 … Cfn)1/n
Conclusion

## Slide 41
Conclusion
Trace Element Spatial Variation Index
TESVI = [(xmax/xmin) / (∑(xmax/xi)/n)] * SD
Trace Element Pollution Index
TEPI = (Cf1 * Cf2 … Cfn)1/n
TESVI and TEPI efficient complementary indices to monitor the pollution in TEs, since they successfully led:
to the ordering of TEs according to the overall spatial variability of their environmental levels along the French Mediterranean littoral;
to the quantification of the global pollution in TEs between monitored sites.
Conclusion

## Slide 42
QUEST
IONS
Thank you for your attention

## Slide 43
Coastal pollution of the Mediterranean
I
N
T
R
O
D
U
C
T
I
O
N
Pollution hot spots (full red circles) along the Mediterranean coasts (EEA 2006)

## Slide 44
I
N
T
R
O
D
U
C
T
I
O
N
Monitoring of the pollution by trace elements
pollution
trace elements

## Slide 45
I
N
T
R
O
D
U
C
T
I
O
N
Monitoring of the pollution by trace elements
pollution
trace elements

## Slide 46
I
N
T
R
O
D
U
C
T
I
O
N
Monitoring of the pollution by trace elements
pollution
trace elements

## Slide 47
TE | Cd | Pb | Cu | Zn | Cr | Fe | Ni
# ref. | 34 | 29 | 27 | 25 | 22 | 14 | 13
TE | As | Se | Ag | Co | Mn | Al | 
# ref. | 3 | 3 | 2 | 2 | 2 | 1 | 
TE | Be | Bi | V | Mo | Sn | Sb | 
# ref. | 0 | 0 | 0 | 0 | 0 | 0 | 
I
N
T
R
O
D
U
C
T
I
O
N
Monitoring
Number of references (1975-2012) on trace elements studied in Posidonia oceanica
Luy et al. (2012; Ecological Indicators)

## Slide 48
World production of trace elements
I
N
T
R
O
D
U
C
T
I
O
N

## Slide 49
World production of trace elements
I
N
T
R
O
D
U
C
T
I
O
N
X 3.1
X 3.1
X 2.0

## Slide 50
World consumption of trace elements
I
N
T
R
O
D
U
C
T
I
O
N
(modified after Sievers et al. 2010)

## Slide 51
Posidonia oceanica
Left: P. oceanica shoots fixed on a plagiotropic rhizome. Right: (A) shoot of leaves on a plagiotropic rhizome; (B, C) adult leaves; (D) intermediate leaf; (E) juvenile leaf (modified after Libes and Boudouresque 1987).
plagiotropic shoot
orthotropic shoot
rhizome
blade
roots
limb
ligula
leaf base (petiole)
E
D
C
B
A
root
leaf base
stipule
scale
rhizome
I
N
T
R
O
D
U
C
T
I
O
N

## Slide 52
Analytical steps:
homogeneous sample
acidic digestion in a microwave oven
measures :
  inductively coupled plasma mass spectrometer
M
A
T
E
R
I
A
L
-
METHODS
Laboratory analyses
Ethos D
ELAN DRCII

## Slide 53
Random list 1:
Be, Al, V, Cr, Mn, Fe, Co, Ni, Cu, Zn, As, Se, Mo, Ag, Cd, Sn, Sb, Pb, Bi
Random list 1:
Sb, V, Sn, Se, Be, Pb, Ni, Mo, Mn, Fe, Cu, Cr, Co, Cd, Bi, Zn, As, Ag, Al
Mean normalization

## Slide 54
Random list 1:
Be, Al, V, Cr, Mn, Fe, Co, Ni, Cu, Zn, As, Se, Mo, Ag, Cd, Sn, Sb, Pb, Bi
Random list 5:
Sb, V, Sn, Se, Be, Pb, Ni, Mo, Mn, Fe, Cu, Cr, Co, Cd, Bi, Zn, As, Ag, Al
Mean normalization

## Slide 55
Random list 5: Sb, V, Sn, Se, Be, Pb, Ni, Mo, Mn, Fe, Cu, Cr, Co, Cd, Bi, Zn, As, Ag, Al
Data pre-treatment

## Slide 56
max diff. 85 %
max diff. 85 %
max diff. 85 %
max diff. 29 %
TEPI comparison