## Slide 1
Public defence of doctoral thesis in Engineering Sciences by
Benoît Pardoen
Supervisor: Frédéric Collin
November 2015
Hydro-mechanical analysis of the fracturing induced by
the excavation of nuclear waste repository galleries
using shear banding

## Slide 2
Long-term management of radioactive wastes
Underground structures
= network of galleries
Context
Deep geological disposal
Repository in deep geological media with good confining properties
(Low permeability
K<10-12 m/s)
Disposal facility of Cigéo project in France
(Labalette et al., 2013)
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 2
Intermediate (long-lived)
&
high activity wastes

## Slide 3
Repository phases
Construction | 
 | Excavation
Maintenance | 
 | Ventilation
Repository | 
 | Sealing
Long term | 
 | Corrosion, heat generation
Type C wastes (Andra, 2005)
Context
Time
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 3

## Slide 4
Excavation Damaged Zone (EDZ)
Fracturing & permeability increase
(several orders of magnitude)
Opalinus clay in Switzerland
(Bossart et al., 2002)
Context
Mechanical fracturing
Excavation
↓
Stress redistribution
↓
Damage / Fracturing
↓
Coupled processes HM property modifications
↓
Safety function alteration
Water transfer
Galleries ventilation
↓
Air-rock interaction
↓
Drainage / desaturation
↓
Modification of the water transfer
Construction
Maintenance
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 4

## Slide 5
Callovo-Oxfordian claystone (COx)
Sedimentary clay rock (France).
- Underground research laboratory
Feasibility of a safe repository
France (Meuse / Haute-Marne, Bure)
(Armand et al., 2014)
Context
Borehole core samples
(Andra, 2005)
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 5

## Slide 6
- Fracturing
Anisotropies: - stress : σH > σh ~ σv
    - material : HM cross-anisotropy.
    Galery // to σh
  Galery // to σH
Issues : Prediction of the fracturing.
Effect of anisotropies ?
Permeability evolution & relation to fractures ?
(Armand et al., 2014)
Context
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 6

## Slide 7
- Air-rock interaction
Large-scale ventilation experiment (SDZ).
Characterise the effect of gallery ventilation on the hydraulic transfer.
Issues: Drainage / desaturation reproduction.
Context
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 7

## Slide 8
Objectives
Better understand, predict, and model the behaviour of the
EDZ in partially saturated clay rock, at large scale.
Fracture description
Fracturing process.
EDZ development.
Constitutive models
Mechanics:
Anisotropic behaviour.
Influence on fracturing.
Coupled:
Hydro-mechanical coupling
(fractures – hydraulic transfer)
Numerical modelling
Finite element method.
Reproduction of fractures
and EDZ in rock.
Influence of fracturing on water transfer around galleries.
Context
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 8

## Slide 9
Context
Fracture modelling with shear bands
Influence of mechanical anisotropy
Permeability evolution and water transfer
Conclusions and perspectives
Outline
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 9
Context
Fracture modelling with shear bands
Influence of mechanical anisotropy
Permeability evolution and water transfer
Conclusions and perspectives

## Slide 10
Shear bands are observed
in many geomaterials.
COx : 75% of fractures
in mode II (shear).
Fracture modelling with shear bands
- Mechanisms of rock mass failure around gallery
(after Diederichs, 2003)
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 10
Axial shortening, ΔH [mm]
Axial load, F [N]
F
Fconf
H
2.1. Material rupture
- Compression test on small sample
Elasticity – No damage
Microcraks – Distributed damage
Coalescence – Localised strain
Fracture
- Fracture modelling
Shear strain localisation
(continuous approach)

## Slide 11
2.2. Shear strain localisation
Brutal concentration of strain in narrow zones
2.2.1. Bifurcation theory
Loss of uniqueness of
localised solutions
Post-peak behaviour related
to strain localisation
Fracture modelling with shear bands
Ductile shear in quartz and pyroxene
(Christopher et al., 2006)
Sand
(Alshibli et al.,
2003)
Sandstones, Muddy Mountains,
Nevada (H. Fossen, 2010)
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 11

## Slide 12
2.2.2. Finite element methods
- Classical FE
Mesh dependency
Need to introduce an internal length
scale for a correct modelling of the
post-peak behaviour.
- Regularisation
Enrichment of the kinematics :
The continuum is enriched with microstructure effects.
Macro-kinematics + micro-kinematics
Macro Ω:
Fracture modelling with shear bands
Equivalent total
deviatoric strain
Micro Ωm:
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 12

## Slide 13
2.2.3. Coupled local second gradient model
- Balance equations
Porous media, biphasic : solid + fluid (Collin et al., 2006)
Unsaturated condition + compressibility of the solid grains (Pardoen et al., 2015)
Balance equations :
Unsaturated Biot’s effective stress :
Solid grain compressibility :
Fracture modelling with shear bands
Microstructure
effects
Kinematic
restriction
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 13

## Slide 14
- Finite elements
Quadrilateral 2D plane-strain
8 nodes for ui and pw
4 nodes for the microkinematic gradient field υij
1 node for the Lagrange multiplier field λij
- Second gradient mechanical law
The double stress Sijk requires a constitutive law.
Linear elastic law function of the (micro) second
gradient of displacement field.
Internal length scale
      D represents the physical
      microstructure
Fracture modelling with shear bands
Unknown
fields
7 d.o.f.
Plasticity
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 14

## Slide 15
2.3. Constitutive models for COx
- Mechanical law - 1st gradient model
Isotropic elasto-plastic internal friction model
Non-associated plasticity, Van Eeckelen yield surface :
φ hardening / c softening
- Hydraulic law
Fluid mass flow (advection, Darcy) :
Water retention and permeability curves (Mualem - Van Genuchten’s model)
Strain localisation
Fracture modelling with shear bands
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 15

## Slide 16
2.4. Gallery excavation modelling
- Numerical model
HM modelling in 2D
plane strain state
Gallery radius = 2.3 m
- Gallery in COx // σh
Effect of stress anisotropy
Anisotropic stress state
pw,0 = 4.5 [MPa]
σx,0 = σH = 1.3 σv = 15.6 [MPa]
σy,0 = σv = 12 [MPa]
σz,0 = σh = 12 [MPa]
- Excavation
Fracture modelling with shear bands
σH
σv
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 16

## Slide 17
- Localisation zone
Incompressible solid grains, b=1
 For an isotropic mechanical behaviour, the appearance and shape of the strain localisation are
mainly due to mechanical effects linked to the anisotropic stress state.
3 days
σr/σr,0 = 0.4
4 days
σr/σr,0 = 0.2
5 days
σr/σr,0 = 0.0
100 days
σ/σ0 = 0.00
1000 days
σ/σ0 = 0.00
Total deviatoric strain
Plasticity
Fracture modelling with shear bands
0
0.06
4.6 m
0.5 m
End of
excavation
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 17

## Slide 18
- Gallery air ventilation :
Water phases equilibrium at gallery wall (Kelvin's law)
Compressibility of the solid grains: b=0.6
Ventilation
pw = -30.7 [MPa]
No ventilation
pw = patm [MPa]
Total deviatoric strain
Plasticity
No ventilation | 
100 days | 1000 days
0
0.184
Ventilation | 
100 days | 1000 days
Fracture modelling with shear bands
suction ↑
σ’ ↑
Elastic unloading
Inhibition of localisation
 Restrain ε
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 18

## Slide 19
- Convergence:
Important during the excavation
Anisotropic convergence
Influence of the ventilation
Experimental results (GED - Andra’s URL)
No strain localisation
Calcul with large D or no loc SDZ? If large D ça rigidifie un peu
Shear band position
Shear bands are necessary for anisotropy
Fracture modelling with shear bands
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 19

## Slide 20
2.5. Conclusions and outlooks
- Conclusions
Reproduction of EDZ with shear bands.
Shape and extent of EDZ governed by anisotropic stress state.
- Next steps …
X Mechanical rock behaviour.
 Material anisotropy, gallery // σH .
X HM coupling in EDZ.
 Influence of fracturing on hydraulic properties.
X Gallery air ventilation and water transfer (drainage / desaturation).
Fracture modelling with shear bands
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 20

## Slide 21
Outline
Context
Fracture modelling with shear bands
Influence of mechanical anisotropy
Permeability evolution and water transfer
Conclusions and perspectives
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 21

## Slide 22
3.1. Anisotropic mechanical behaviour
Sedimentary rocks with bedding planes …
 Cross-anisotropy
Behaviour depends on:
- the microstructure
- the loading direction
Influence of mechanical anisotropy
Zion National Park – Utah
S. Smith, pbase.com
riosuerte.com
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 22

## Slide 23
- Linear elasticity :
Cross-anisotropic (5 param.) + Biot’s coefficients
- Plasticity :
Cohesion anisotropy with fabric tensor
Cross-anisotropy
Influence of mechanical anisotropy
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 23

## Slide 24
3.3. Gallery excavation modelling for isotropic initial stress state
Effect of material anisotropy
Isotropic stress state
σ =12 MPa
- Anisotropy effect on strain localisation
Localisation at the end of excavation
Increase of anisotropy
 For isotropic stress state, strain localisation is triggered
if a sufficient material anisotropy is considered.
Influence of mechanical anisotropy
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 24

## Slide 25
- Cohesion evolution
Anisotropy:
Initially : isotropic σij 
Excavation : σr ↓ and σort ↑
t = 15.4 days | t = 16.8 days | t = 21 days | t = 21 days
Influence of mechanical anisotropy
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 25

## Slide 26
4.5m
3.3. Gallery excavation modelling for anisotropic initial stress state
- Stress state
Major stress in the axial direction σx,0 = σh = 12.40 MPa
Gallery // to σH σy,0 = σv = 12.70 MPa
σz,0 = σH = 1.3 x σh = 16.12 MPa
- Shear banding
Total deviatoric strain
 Shape modification due to σH
0
0.05
3m
Horizontal
Vertical
- Convergence
 Long-term deformation
Experimental
Numerical
Influence of mechanical anisotropy
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 26
 Creep deformation

## Slide 27
- Creep deformation
Permanent strain
In the long term
Under constant stress
below the yield strength
- Viscosity
Time-dependent plastic strain
(Jia et al., 2008; Zhou et al. 2008)
Horizontal
Vertical
- Convergence
 Viscosity
effect
σ1
σ3
Influence of mechanical anisotropy
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 27

## Slide 28
3.4. Conclusions and outlooks
- Conclusions
Reproduction of EDZ in both directions.
Shape and extent of EDZ governed by:
- anisotropic stress state.
- anisotropic mechanical behaviour.
Long-term convergence with viscosity.
- Next steps …
X HM coupling in EDZ.
 Influence of fracturing on hydraulic properties.
X Gallery air ventilation and water transfer.
GED
// σh
GCS
// σH
Influence of mechanical anisotropy
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 28

## Slide 29
Outline
Context
Fracture modelling with shear bands
Influence of mechanical anisotropy
Permeability evolution and water transfer
Conclusions and perspectives
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 29

## Slide 30
Permeability evolution and water transfer
4.1. Large-scale experiment of gallery ventilation (SDZ)
Characterise the effect of gallery ventilation
on the hydraulic transfer around it.
 drainage / desaturation
 exchange at gallery wall
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 30

## Slide 31
4.2. Permeability variation in fractured zone
HM coupling in the EDZ.
4.2.1. Saturated permeability in boreholes
Fracture and rock matrix permeabilities
 Capture kw evolution
 Relation to fractures
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 31
Permeability evolution and water transfer

## Slide 32
4.2.2. Evolution of intrinsic water permeability
Various approaches: deformation, damage, cracks…
- Relation to deformation
Volumetric effects = increase of porous space
()(
(Kozeny-Carman)
- Fracture permeability
Cubic law for parallel-plate approach
(Witherspoon 1980; Snow 1969, Olivella and Alonso 2008)
Poiseuille flow (laminar flow)
equivalent Darcy’s media
- Empirical law
Related to strain localisation effect
Permeability variation threshold
Localised deformation
Fracture initiation
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 32
Permeability evolution and water transfer

## Slide 33
4.3. Hydraulic boundary condition for exchanges at gallery wall
- Classical approach
Instantaneous equilibrium (Kelvin’s law)
- Experimental
Drainage / desaturation  Progressive hydraulic transfer & equilibrium
- Non-classical mixed boundary condition
Liquid water + water vapour
- Seepage flow :
Evaporation flow :
(Nasrallah and Perre, 1988)
Sr,w = 1
Sr,w < 1
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 33
Permeability evolution and water transfer

## Slide 34
4.4. Modelling of excavation and SDZ experiment
4.4.1. HM coupling in EDZ
- Gallery excavation
SDZ  GED gallery // σh
Anisotropic σij,0 and material
 Localisation zone dominated
by stress anisotropy
- Intrinsic permeability evolution
Cross-sections
Plastic strain and a part of the elastic one  EDZ extension + kw increase
Plasticity Total deviatoric strain
kw,,ij / kw,ij,0 [-]
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 34
Permeability evolution and water transfer

## Slide 35
4.4.2. Modelling of the SDZ experiment
- Water pressure in the cavity air
pw (suction) corresponding
to RH and T (Kelvin’s law).
Imposed at gallery wall through hydraulic boundary condition.
Excavation (RH=100%)  Initiation phase  Ventilation
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 35
Permeability evolution and water transfer

## Slide 36
Experimental
Numerical
- Drainage / pw reproduction
Oblique 45° Horizontal
αv = 10-3 m/s
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 36
Permeability evolution and water transfer

## Slide 37
- Desaturation EDZ / w reproduction
Horizontal boreholes
 Desaturation: overestimation in long term
 Vapour transfer (αv = 10-3 m/s)
 Good reproduction at gallery wall
At gallery wall
Permeability evolution and water transfer
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 37

## Slide 38
- Exchanges at gallery wall
Flows:
Water pressure in cavity:
 Transfer depends on αv
Permeability evolution and water transfers
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 38

## Slide 39
Outline
Context
Fracture modelling with shear bands
Influence of mechanical anisotropy
Permeability evolution and water transfer
Conclusions and perspectives
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 39

## Slide 40
Conclusions and perspectives
Conclusions
Better understand, predict, and model
the behaviour of the EDZ in partially
saturated clay rock, at large scale.
Contribution : Provide new elements for the prediction and understanding of the HM behaviour of the EDZ.
Innovations : Fracturing process is predicted on a large scale with shear bands.
Strain localisation effects are taken into account in coupled processes (water flow).
Fracture description
EDZ with strain localisation.
Constitutive models
Mechanics: anisotropy, viscosity.
Coupled: fracture influence on permeability.
Numerical modelling
Shape, extent.
Influence of fracturing, permeability variation, anisotropy.
Water transfer.
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 40

## Slide 41
Perspectives
.
Fracture description
Tensile fracture (mode I).
Shrinkage / dessication cracks.
Fracture closing,
sealing / healing.
Constitutive models
Mechanics:
- Extension criterion.
Coupled:
- Influence of drying on fracturing.
- Permeability in tensile cracks.
Numerical modelling
3D modelling with regularisation method.
Extend to other materials and applications.
(Ta, 2009)
Context | Fracture modelling | Anisotropy | Water transfer | Conclusion | 41
Conclusion and perspectives

## Slide 43
APPENDICES

## Slide 44
 |  |  |  |  | 44
5 m
12 m
12 m
5 m
R: 2.3 m
z
y
x
z
x
y
- Fracturation = 3D problem
Fractures pattern around
a gallery in Boom clay
- Mesh:
Mechanical modelling in 3D state.
Classical FE, no regularisation method.
Gallery excavation in 3D

## Slide 45
 |  |  |  |  | 45
Gallery excavation in 3D
- Localisation zone:
Equivalent deformation εeq during boring.
3.75 days | 4 days | 4.25 days
σ/σ0 = 0.25 | σ/σ0 = 0.20 | σ/σ0 = 0.15
3 days | 3.25 days | 3.5 days
σ/σ0 = 0.40 | σ/σ0 = 0.35 | σ/σ0 = 0.30
0
0.025
z
y
x

## Slide 46
 |  |  |  |  | 46
Gallery excavation in 3D
- Localisation zone:
Equivalent deformation εeq during boring.
z
y
3 days | 3.25 days | 3.5 days
σ/σ0 = 0.40 | σ/σ0 = 0.35 | σ/σ0 = 0.30
3.75 days | 4 days | 4.25 days
σ/σ0 = 0.25 | σ/σ0 = 0.20 | σ/σ0 = 0.15
0
0.025

## Slide 47
 |  |  |  |  | 47
- Localisation zone
Equivalent deformation εeq - for 4.25 days of excavation (σ/σ0 = 0.15) :
z<0 : excavation zone
z=0 : gallery front
z>0 : rock mass
Gallery excavation in 3D
z=-2.25m | z=-1.25m | z=-0.25m | z=+0.25m | z=+1.25m
0
0.025
x
y

## Slide 48
0
0.184
Biot’s coefficient: b=0.6
Plasticity
Compressibility influence on shear banding
3 days
σr/σr,0 = 0.4
4 days
σr/σr,0 = 0.2
5 days
σr/σr,0 = 0.0
100 days
σ/σ0 = 0.00
1000 days
σ/σ0 = 0.00
End of
excavation
Total deviatoric strain
Plasticity
b=0.6 b=1
4 days 5 days 4 days 5 days
 |  |  |  |  | 48

## Slide 49
- Gallery air ventilation :
Total deviatoric strain
Plasticity
0
0.184
suction ↑
σ’ ↑
Elastic unloading
Inhibition of
localisation
 Restrain ε
 |  |  |  |  | 49
Air ventilation influence on shear banding
Ventilation | 
100 days | 1000 days

## Slide 50
- Spatial discretisation
Matricial form of balance equations:
vector of the unknown increments of nodal variables
- Element stiffness matrix
Unsaturated condition, Sr,w
Soild phase compressibility, b
Permeability anisotropy and evolution, kw,ij
Finite element formulation – 2d gradient model
 |  |  |  |  | 50
Unknown
fields
7 d.o.f.

## Slide 51
 |  |  |  |  | 51
Second gradient mechanical law – Influence of the elastic modulus
Plasticity
Total deviatoric strain
D = 80 N D = 20 N D = 5 N
- Second gradient mechanical law
Linear elastic law function
Independent of pw
Internal length scale
      D represents the physical
      microstructure
 D should be evaluated based on experimental measurements
 Better numerical precision if a few elements compose the shear band width
 Large scale …

## Slide 52
Cross-anisotropic elasticity
Linear elasticity (5 param.)
Biot’s coefficients
Micro-homogeneity and micro-isotropy assumptions (Cheng, 1997)
for which Ks is homogeneous and isotropic at grains scale.
 |  |  |  |  | 52
Influence of mechanical anisotropy

## Slide 53
Anisotropic plasticity with fabric tensor
Cohesion anisotropy with fabric tensor.
c0 is the projection of the tensor on a generalised unit loading vector :
Deviatoric part:
Generalisation with higher order tensor:
Orthotropy:
Cross-anisotropy:
 |  |  |  |  | 53
Influence of mechanical anisotropy

## Slide 54
Viscosity
Time-dependent plastic strain, delayed plastic deformation
Progressive evolution of the material microstructure or to mechanical properties degradation (damage)
Viscoplastic loading surface and potential surface:
Delayed viscoplastic hardening function:
 |  |  |  |  | 54
Viscosity

## Slide 55
Permeability evolution and water transfer
- Reproduction at the end of excavation
(a) Volumetric strain
(b) Equivalent deviatoric
total strain
(c) Equivalent deviatoric
plastic strain
(d) Plastic strain and a
part of the elastic one
 EDZ extension
 kw increase
 |  |  |  |  | 55

## Slide 56
- Drainage / pw reproduction
Horizontal Oblique 45°
Vertical Horizontal
αv = 10-3 m/s
 Good matching
 HM effect - kw,h> kw,v
 |  |  |  |  | 56
Permeability evolution and water transfer

## Slide 57
- Desaturation EDZ / w reproduction
At gallery wall
Low vertical drainage
kw,h > kw,v : kw,h/v = 4 10-20 / 1.33 10-20 [m²]
 |  |  |  |  | 57
Vertical
kw,,ij / kw,ij,0 [-]
Permeability evolution and water transfer

## Slide 58
- Convergence
Total deviatoric strain
Velocity norm
Diametrical
convergence
 |  |  |  |  | 58
σr/σr,0 = 0.04
t = 16.8 days
σr/σr,0 = 0.00
t = 21 days
σr/σr,0 = 0.08
t = 15.4 days
Mechanical anisotropy

## Slide 59
Kinetics of drying process – Mixed boundary condition
- Non-classical mixed boundary condition
Progressive thermodynamic equilibrium by vapour transfer.
Vapour transfer in a boundary layer.
- Non-classical mixed boundary condition
Liquid water + water vapour
- Seepage flow :
Evaporation flow :
(Nasrallah and Perre, 1988)
 |  |  |  |  | 59
Evaporation and seepage flows at gallery wall for a
constant air ventilation (Gerard et al., 2008).

## Slide 60
Kinetics of drying process – Water vapour transfer
Drying test : saline solutions (control vapour phase & RH), or convective drying tests
Drying flux curve:
Thermo-hydraulic process and exchanges in a boundary layer.
1. Preheating
2. Constant flux : heat totally used for water evaporation, saturated boundary layer, external conditions (RH, T, v).
3. Decrease of the flow : internal resistances restrict the water outflow, desaturation of the boundary layer
 αv depends on external drying conditions (RH, T, v)
 |  |  |  |  | 60
Drying vapour flux, E
Water content, w
Surface temperature, T
Time, t
Water mass, Mw
Time, t

## Slide 61
Gallery excavation modelling for anisotropic initial stress state
Gallery // to σh
Convergence and HM coupling
 |  |  |  |  | 61
Close to gallery wall:
Strong effect of the localisation bands
σΓ=cst, pw↑, σ’↓ , εpl↑ (on the yield surface)
Convergence keep increasing
In the vertical: similar
Vertical cross-section

## Slide 62
- Displacements
Andra’s URL Mine-by experiment
Borehole – extensometers and pore pressure  Characterise the displacements in the rock mass
Mine-by experiment
 |  |  |  |  | 62

## Slide 63
- Displacements
Viscosity based on creep tests
- Convergence
Horizontal
Vertical
Horizontal
Vertical
 |  |  |  |  | 63
Mine-by experiment

## Slide 64
- Displacements
Viscosity based on in situ measurements  Viscosity influence
- Convergence
Horizontal
Vertical
Viscosity allows to reproduce the increase
of convergence in the long term.
Horizontal
Vertical
 |  |  |  |  | 64
Mine-by experiment

## Slide 65
- Pore water pressure
Mine-by test
After excavation: RH=100% , pw = 0 MPa in the gallery
Horizontal:
 |  |  |  |  | 65
Mine-by experiment