## Slide 1
The CHEOPS mission: towards exoplanet characterisation
Valérie Van Grootel
FNRS Research Associate
Université de Liège
and the CHEOPS science team

## Slide 2
SCIENTIFIC MOTIVATION

## Slide 3
The transit technique
(ex. CoRoT, Kepler)
(primary eclipse)
(secondary eclipse)
CHEOPS: CHaracterizing ExOPlanet Satellite
The radial velocity technique
(ex. HARPS, ESPRESSO)
➨ radius of the planet Rp
➨ minimum mass
Mp sin(i)
Mp & Rp ➨
Planet average density ρp

## Slide 4: What are exoplanets made of?
Earths
(~1 RT)
Neptunes
Saturnes and Jupiters
(~10 RT)
(~4 RT)

## Slide 5: What are exoplanets made of?
Earths
(~1 RT)
Neptunes
Saturnes and Jupiters
(~10 RT)
(~4 RT)
⬇
Super-Earths
(ex. CoRoT-7b,
HD97658b)
⬇
Subgiants
(ex. CoRoT-8b, HD149026b)
Notes: On ne connaît que qques super-Earths avec M+R !

## Slide 6: What are exoplanets made of?
Constraints based on bulk densities
⬇
inversion techniques

## Slide 7
Ex. the super-Earth HD97658b
Van Grootel et al. 2014, models from D. Valencia
Rocks > 60%
Ices 0-40%
H-He 0-2%
R=2.25 RE

## Slide 8
Targets: bright stars
radial velocity
CHEOPS
CHEOPS optical bandpass: 400-1100 nm

## Slide 9
CHEOPS strategy: follow up mission
Detect the transit of known super-Earths
Ground-based RV surveys
HARPS, HARPS-N, HIRES, SOPHIE (on going)
ESPRESSO (2017)
Measure accurate light curves for Neptunes
Ground-based transit surveys
NGTS (2014)
TESS
(2017)
K2
(2014)

## Slide 10
CHEOPS: what can we expect?
 | #planets (targets) | #transits
On-going RV surveys | 60–80 | 4–5
Future RV surveys | 105–140 | 5–7
Ground-based transit surveys | ~60 | (~60)
TESS and K2 | ??? | ???

## Slide 11
CHEOPS: hoped legacy
JWST (~2018)
E-ELT, GMT, TMT
(~2020-2025)
Golden targets for future atmospheric characterization

## Slide 12
How to model the host stars
Mass, radius, and age

## Slide 13
Rp α R*
Mp α M*2/3
+ the age of the star is the best proxy for the age of its planets
(Sun: 4.57 Gyr, Earth: 4.54 Gyr)
Radial velocities
Transits
Why is stellar characterization so important?
Direct technique: interferometry (R*)
Indirect techniques: GAIA parallaxes (R*), stellar evolution modeling (M*, R*, age), asteroseismology (M*, R*, age), transit light curve (ρ*)
Main sequence nearby bright solar-like stars (6<V<12): G and K-types

## Slide 14
Available now:
CHARA (Mount Wilson USA, 330-m baseline)
VLTI (Chile, 150-m baseline)
By the launch of CHEOPS: MROI (New Mexico, 400-m baseline)
To get R* to ~ 1-2%
(depending on size, distance and magnitude of the star)
Stellar characterization: Interferometry

## Slide 15
To get R* to ~ 1-2%
(normally not affected by GAIA’s stray light issues)
Independently from interferometry  increase the accuracy on stellar radius
Method:
Π: parallax
Av: interstellar extinction
BC: bolometric correction
Teff: effective temperature
Stellar characterization: GAIA parallaxes

## Slide 16
To get R*, M* and age
Delrez, Van Grootel et al. (2014)
Teff, Z (from spectroscopy); Z~[Fe/H] (better if other abundances)
log g (spectroscopy), and/or ρ* (transits), and/or L* (parallax)
Inputs:
Stellar evolution codes: CLES (Liege), MESA (open source),…
Stellar characterization: stellar evolution modeling

## Slide 17
To get R*, M* and age
General method, always applicable
Only require spectroscopic information, generally available
Get R*, M* and age
Pros:
Cons:
Not very precise and model-dependent
Providing ~50 K on Teff, 0.05 dex on [M/H] and 1% on L* (GAIA):
R* to ~ 1-2%
M* to ~ 5-10%
Age to 2-4 Gyr
Main uncertainties: from stellar interiors (helium initial abundance, efficiency of convection, importance of mixing processes)
Will be improved in the coming years from bulk asteroseismic results from CoRoT and Kepler ?
Stellar characterization: stellar evolution modeling

## Slide 18
To get R*, M* and age
Principle:
Use stellar oscillations to constrain stellar interiors and to get structural parameters
For solar-like stars, main seismic indicators:
the large separation Δν (α ρ*), frequency at maximum power νmax (α g/Teff0.5), small separations δν (α age)
Stellar characterization: Asteroseismology

## Slide 19
For CHEOPS targets:
Low-quality seismic data: only Δν~ρ* to 5%
ρ* + R* (~1-2% by parallaxes/interferometry)
 M* to 8-10%
Mid-quality seismic data: 1-month TESS, ground-based (ESPRESSO)
- Δν~ρ* to 0.5% (V=6) + R* (~1-2% by parallaxes/interferometry)
 M* to ~3-4%
- Δν~ρ* to 2% (V=9) + R* (~1-2% by parallaxes/interferometry)
 M* to ~5%
Age still difficult to do better than 2-4 Gyr
High-quality seismic data: not for CHEOPS  (waiting for PLATO )
R* ~ 1-2%, M* ~ 2-4%, age ~ 10% (!)
Stellar characterization: Asteroseismology

## Slide 20
Why is stellar characterization so important?
Progress on this side ?
Dorn et al. 2015, arXiv 150203605D

## Slide 21
ESA’s FIRST SMALL MISSION

## Slide 22
ESA S-class mission in Cosmic Vision 2015-2025:
Science: top rated science in any area of space science
Cost:
  total cost <150 M€ (~ 110 M€)
  cost to ESA: 50 M€ (platform, detector, launch)
Schedule:
  developed and launched within 4 years
call issued | March, 2012
proposal due | June, 2012
mission selection | October, 2012
mission adoption | February, 2014
launch | end 2017
Nominal lifetime | 3.5 years
ESA small mission requirements

## Slide 23
Switzerland
Mission Lead
Instrument Team
Science Operations Center
Germany Focal Plane Assembly
Italy Optics
Austria Digital Processing Unit
Hungary Radiators
Belgium Baffle, Door
Sweden Data simulator
UK Quick look
France Data Reduction Software
Portugal Mission Planning, Archive, & Data Reduction Software
CHEOPS consortium
A. Fortier
RINGBERG
WORKSHOP
Spain Mission operations centre
Willy Benz
PI, U. Bern

## Slide 24
600—800 km
CHEOPS orbit
Sun
120°
OBSERVATIONS
35°

## Slide 25
CHEOPS science requirements

## Slide 26
CHEOPS: Instrument
SPIE
CONFERENCE
A. Fortier
300 mm
Instrument Design
outer baffle
inner
baffle
secondary
mirror
primary
mirror
structure tube
radiators
BEO
CCD
FPA
Ritchey-Chrétien telescope
primary mirror internal baffle
COSPAR
CONFERENCE
EPSC2014
CONFERENCE

## Slide 27
Primary structure
CIS payload
Body-mounted solar array
S-band antenna
Fixed sunshield
Star Trackers Optical Heads
Secondary Structure
CHEOPS: Instrument
A. Fortier
Accommodation on the Spacecraft
S/C contractor: ECE-CASA
On-board data stacking
Measurement cadence: 1 min-1 Telemetry: 1.2 Gbit/day
RINGBERG
WORKSHOP

## Slide 28
CHEOPS baffle @Centre Spatial de Liègeinstrument
External baffle @Liege

## Slide 29
CHEOPS (33cm mirror)
CoRoT (27cm mirror)
Identical pieces

## Slide 30
CHEOPS
COROT
On the same shaker @ CSL

## Slide 31
Summary
CHEOPS is Europe’s next exoplanet mission (2017)
CHEOPS is a follow-up machine: Knowing when to look at a star makes CHEOPS extremely efficient: ➡ Provides Mp and Rp for super-Earths, Neptunes and subgiant planets ➡ Collects the golden targets for future in-depth and atmospheric characterization (JWST, E-ELT,…)
More information in:
http://cheops.unibe.ch/
http://sci.esa.int/cosmic-vision/49469-cheops/
CHaracterizing ExOPlanet Satellite

## Slide 32
The transit technique
(ex. CoRoT, Kepler)
(primary eclipse)
(secondary eclipse)
CHEOPS: CHaracterizing ExOPlanet Satellite
The radial velocity technique
(ex. HARPS, ESPRESSO)
➨ radius of the planet Rp
➨ minimum mass
Mp sin(i)
Mp & Rp ➨
Planet average density ρp
Bright targets are needed!

## Slide 33
CHEOPS targets
100 ppm
6 hours
radius precision up to 10% (bulk density to 30%)
S/Ntransit = 5
Photometric accuracy: super-earth detection
6 < V < 9, G5 dwarf stars, Pplanet~ 50 days
☛ Transit detection of super-earths
20-ppm precision over 6-h transit
(w/ 50% interruptions)
super-earth ➡︎

## Slide 34
CHEOPS targets
♆
3 hours
2500 ppm
☛ Characterisation of neptune transit light curves
85-ppm precision over 3-h transit (w/ 20% interruptions)
Photometric accuracy: neptune characterisation
9 < V < 12, K dwarf stars, Pplanet~ 13 days
➡ radius better than 10%
➡S/Ntransit = 30
♆