## Slide 1: Quantification of Nitrogen Stress on Winter Wheat by Multispectral Vision based on Reflectance Measurements and Textural Descriptors
MARLIER Ga., GRITTEN Fa., FRAIPONT Gb., LEEMANS Vac., DUMONT Bbc ., DESTAIN M-Fa., MERCATORIS Bac.
a : Université de Liège – Gembloux Agro-Bio Tech. Biosystems Engineering Dept. Precision Agriculture unit.
b : Université de Liège – Gembloux Agro-Bio Tech. AgroBioChem Dept.,
Engineering Plant Production and Valorization Unit
c : Université de Liège – Gembloux Agro-Bio Tech. TERRA Research unit,
AgricultureIsLife

## Slide 2: Context
Precision Agriculture
  Spatial and temporal variability on field
  Nitrogen optimizing
    Essential and limiting element for plants
Measurement and sensors
Design support system
Equipment optimization
Context
State of the art
Materials and methods
Results
Conclusions
Objective

## Slide 3: State of the art
Estimation of nitrogen content
  Tissue analysis
    Kjeldahl method or Dumas combustion
    Reliable BUT destructive and time consuming
  Optical analysis
    Transmission, absorption and reflection
    Depend on leaves components and wavelengths
Context
State of the art
Materials and methods
Results
Conclusions
Objective

## Slide 4: Optical methods
Hand-held device
  Measurements of small part of leaf
Leaf level
Canopy level
Chlorophyll
Nc
Water
  Absorbance
  Reflection
Reflectance
Ranking
  Remote
  Proxi
  Satellite – Drone – Ground
  Hyperspectral
  Multispectral
  Active
  Passive
  Light source
Context
State of the art
Materials and methods
Results
Conclusions
Objective

## Slide 5: Objective
Determination of the nitrogen concentration in leaves with multispectral device
Need measurement
Fast
All growing season
Optical device
Canopy level
Multispectral
Reliable and accurate
Continuous
Non-destructive
Passive
Image analysis
Wavelengths selection
Parameters selection
Context
State of the art
Materials and methods
Results
Conclusions
Objective

## Slide 6: Materials and Methods (AgricultureIsLife)
Field experiment (Gembloux, Belgium, Temperate climate, Lat. : 50.56°N., Lon. : 4.68°E.)
Growing season 2013-2014 (3 outputs on field) and 2015-2016 (until now 1 output on field)
Winter wheat : Triticum aestivum L.
Estimation of nitrogen content in leaves
  Reference method
    Kjeldahl method
    Process : Digestion (sulfuric acid). distillation and titration for NH4+ estimation.
        0.2g of dry matter (leaves)
        Selection of leaves visulized by camera
        1 sample by plot
  M SPAD measurements (only for 2014 season)
      Hydro N-Tester. Yara international ASA.
      Norway.
      Transmittance in 650 nm and 950 nm
      15 leaves measured in each plot
Context
State of the art
Materials and methods
Results
Conclusions
Objective

## Slide 7: Multispectral device
Filter wheel: 450 nm to 950 nm and 2 width bands (≈50 nm and ≈100 nm)
Monochrome camera (CMOS, BCi5, C-Cam Technologies, Belgium)
White reference: Taking into account variation of natural illumination  regulation of integration time
Context
State of the art
Materials and methods
Results
Conclusions
Objective

## Slide 8: Image pretreatment
Background correction
Reference
Corrected image
Raw image
Context
State of the art
Materials and methods
Results
Conclusions
Objective

## Slide 9: Image pretreatment
Segmentation
  Discrimination of PAL (Photosynthetically Active Leaves) by using Bayes’ Theorem
Image
Segmented image
Context
State of the art
Materials and methods
Results
Conclusions
Objective
PAL
Soil
White reference

## Slide 10: Image Analysis
Leaf :
  mean of reflectance of PAL
Canopy :
  Leaf area
  Textural parameter
    Gray Level Co-occurrence Matrix (GLCM)
      Contrast
      Correlation
      Energy
      Homogeneity
    Fourier transform (FFT2D)
      Standardized dispersion coefficient derived from frequency content of images on X axis and Y axis
Context
State of the art
Materials and methods
Results
Conclusions
Objective

## Slide 11: Gray Level Co-occurrence Matrix (GLCM)
  Contrast
    Range [0 65025]
  Correlation
    Range [-1 1]
  Energy
    Range [0 1]
  Homogeneity
    Range [0 1]
Context
State of the art
Materials and methods
Results
Conclusions
Objective
E=0,5
H=0,0039

## Slide 12: Fourier Transform 2D
Standardized dispersion coefficient
On X axis : 2.8*
On Y axis : 1.8*
On X axis : 4.3*
On Y axis : 2.8*
Unit : intensity*pixel²
Image
Amplitude of FT2D
Context
State of the art
Materials and methods
Results
Conclusions
Objective

## Slide 13: Data analysis
Partial Least Square regression (PLS) :
  Determination of the correlation between Nc and the filter response
  Transformation of set of 22 filters to smaller set of uncorrelated components
Best Subset regression : Determination of the most relevant filters assessing the Nc
Context
State of the art
Materials and methods
Results
Conclusions
Objective

## Slide 14: Results
Leaf Nc through growing seasons
Nc from 1.51 % to 3.92%
Chart: Nitrogen concentration in leaves
| 42513 | 42513 | 42520 | 42520 | 42527 | 42527 | 42471 | 42471 | 42471 | 42471
0-0-0 _ both season | 2.918 | 3.519 | 2.7 | 3.081 | 3.433 | 3.263 | 1.6149 | 1.527 | 1.5177 | 1.5495
60-60-60 _ both season | 3.206 | 3.349 | 3.341 | 3.325 | 3.842 | 3.555 | 2.2123 | 2.1435 | 2.0664 | 2.0851
30-30-90 _ 2014 season | 3.699 | 3.358 | 3.356 | 3.321 | 3.778 | 3.825
50-40-65 _ 2014 season | 3.917 | 3.592 | 3.402 | 2.839 | 3.732 | 3.875
30-60-90 _ 2016 season | 1.5763 | 1.7977 | 1.7465 | 1.7518
90-30-60 _ 2016 season | 2.2808 | 2.2178 | 2.3078 | 2.2677
30-90-60 _ 2016 season | 1.8723 | 1.5377 | 1.9044 | 1.8249
2016 growing season
2014 growing season
Context
State of the art
Materials and methods
Results
Conclusions
Objective

## Slide 15: Results (in 2013-2014)
Relationship between Nc and M SPAD values
  Determination coefficient: R²=53%
  R² improving by computing indices
Context
State of the art
Materials and methods
Results
Conclusions
Objective

## Slide 16: Results
Mean reflectance of PAL in function of wavelengths
Chart: Mean reflectance for 11/04/2016 output
| 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 850 | 900 | 950
mod1_BF | 0.10221 | 0.12782 | 0.16876 | 0.16933 | 0.14532 | 0.2852 | 0.55976 | 0.63069 | 0.65975 | 0.68004 | 0.65043
mod2_BF | 0.09919 | 0.11186 | 0.13343 | 0.13359 | 0.11755 | 0.24003 | 0.53637 | 0.62783 | 0.66891 | 0.6763 | 0.64715
mod3_BF | 0.097155 | 0.11268 | 0.1389 | 0.14134 | 0.12021 | 0.25505 | 0.54739 | 0.62408 | 0.66344 | 0.67695 | 0.65088
mod4_BF | 0.098382 | 0.11733 | 0.15102 | 0.15682 | 0.12999 | 0.27168 | 0.54435 | 0.6204 | 0.66185 | 0.67254 | 0.64772
mod5_BF | 0.097785 | 0.10922 | 0.12986 | 0.13135 | 0.11452 | 0.24398 | 0.54591 | 0.6441 | 0.68224 | 0.69294 | 0.66774
mod1_NF | 0.097871 | 0.10649 | 0.15629 | 0.12962 | 0.10704 | 0.18638 | 0.58184 | 0.6638 | 0.69051 | 0.72889 | 0.66422
mod2_NF | 0.097559 | 0.10023 | 0.12606 | 0.10595 | 0.096556 | 0.13577 | 0.56515 | 0.66045 | 0.68831 | 0.72646 | 0.65787
mod3_NF | 0.099165 | 0.099485 | 0.13462 | 0.10832 | 0.096394 | 0.14662 | 0.56562 | 0.64728 | 0.68373 | 0.71789 | 0.65296
mod4_NF | 0.09664 | 0.1018 | 0.13928 | 0.1148 | 0.10237 | 0.16081 | 0.57079 | 0.64756 | 0.68489 | 0.71704 | 0.66287
mod5_NF | 0.098606 | 0.10006 | 0.12314 | 0.10353 | 0.096611 | 0.13328 | 0.5797 | 0.67539 | 0.7104 | 0.74133 | 0.68595
Context
State of the art
Materials and methods
Results
Conclusions
Objective

## Slide 17: Results
Leaf area
  Regression analysis of nitrogen content in function of leaves area
  (R²=40.5%)
Chart: Nc actual (Kjeldahl) [%]
| 0 | 4.5
 | 0 | 4.5
Context
State of the art
Materials and methods
Results
Conclusions
Objective

## Slide 18: Results
Partial Least Square regression
Partial Least Square regression (PLS) |  |  | 
Parameters | Number of components for optimal model | Determination coefficient (R²) (%) | Determination coefficient predicted (R²pred) (%)
Reflectance | 7 | 92.41 | 89.79
Contrast | 10 | 87.88 | 84.18
Correlation | 6 | 83.8 | 79.7
Energy | 3 | 80.7 | 71.5
Homogeneity | 5 | 92.3 | 91.8
Standardized dispersion coefficient on X (FFT2D) | 5 | 92 | 90.4
Standardized dispersion coefficient on Y (FFT2D) | 5 | 92.2 | 90.7
Context
State of the art
Materials and methods
Results
Conclusions
Objective

## Slide 19: Results
Best Subset Regression
Best Subset Regression |  |  | 
Parameters | 4 relevant filters | determination coefficient (R²) (%) | determination coefficient predicted (R²pred) (%)
Reflectance | 450±40; 700±25; 800±50;850±50 | 89.1 | 88.5
Contrast | 450±25;550±25; 850±50;900±20 | 80 | 78.7
Correlation | 450±40;600±40; 850±20;900±20 | 81.1 | 78.6
Energy | 500±20;650±40; 750±20;750±40 | 83.6 | 82.7
Homogeneity | 500±20;600±40; 650±40;800±25 | 91.6 | 91.1
Standardized dispersion coefficient on X (SDCX) | 450±25;500±40; 700±25;750±40 | 88.5 | 88
Standardized dispersion coefficient on Y (SDCY) | 450±25;500±40; 700±25;750±40 | 88.9 | 88.4
Context
State of the art
Materials and methods
Results
Conclusions
Objective

## Slide 20: Results
4 chosen filters : 450±40nm; 600±40nm; 700±25nm and 850±50nm
Regression analysis : step by step
Optimal model :
Filters | Parameters |  |  |  |  |  |  | 
 | Reflectance | Contrast | Correlation | Energy | Homogeneity | SDCX | SDCY | Leaf Area
450±40nm | X |  |  |  | X |  | X | 
600±40nm | X | X |  |  | X | X | X | 
700±25nm | X |  | X | X |  |  |  | 
850±50nm |  | X |  |  |  |  |  | 
Context
State of the art
Materials and methods
Results
Conclusions
Objective

## Slide 21: Results
Actual and predicted nitrogen content
  R² = 93.97 %
  R²pred = 93.18%
Chart: Nc (Kjeldahl) (%)
diagonal | 0 | 4.5
Linear relationship
Context
State of the art
Materials and methods
Results
Conclusions
Objective

## Slide 22: Conclusions
Estimation of Nitrogen content in leaves at canopy level
Selection of relevant filters
  Reflectance
  Textural parameters
    Gray level Co-occurrence Matrix (GLCM)
    Standardized dispersion coefficient from frequency content of image
  Determination coefficient of model built
    R² = 93.97 %
    R²pred = 93.18 %
Further work : increasing set of data
Context
State of the art
Materials and methods
Results
Conclusions
Objective

## Slide 23
Thank you for your attention
Guillaume Marlier
PhD Student. Université de Liège. Gx Agro-Bio Tech
E-mail: Guillaume.Marlier@ulg.ac.be
Precision Agriculture unit
  Pr. Dr. Ir. DESTAIN Marie-France
  Dr. Ir. LEEMANS Vincent
  Dr. Ir. MERCATORIS Benoit
Engineering Plant Production and Valorization unit
(Crop Science in temperate regions)
  Dr. Ir. DUMONT Benjamin
  Ir. FRAIPONT Guillaume