## Slide 1: EXPERIMENTAL INVESTIGATIONS OF THE VALORIZATION OF THE EXHAUST WASTE HEAT OF A GASOLINE ENGINE BASED ON A RANKINE CYCLE
Olivier Dumonta, Arnaud Legrosa, Mouad Dinyb & Vincent lemorta
a University of Liege (Belgium)
b PSA Groupe, Direction Recherche et Dévelopement (France)

## Slide 2: Introduction Table of content
Introduction
Pump
Conclusions and prospects
Heat exchangers
Expander

## Slide 3: Introduction Context
Energy transition in the transport sector
World convergence on CO2 emissions limitations
Decrease of other polluants emissions (CO, HC, NOx)
Interest for the Rankine cycle
[] Energies;ISSN 1996-1073 4, Comparison and impact of waste heat recovery technologies on passenger car fuel consumption on a normalized driving cycle. 8 Legros Arnaud Guillaume Ludovic , Diny Mouad , Zaïdi Hamid and Lemort Vincent

## Slide 4: Introduction Test-rig
Test-rig of an open-loop Rankine cycle with exhaust gas waste heat recovery
Gasoline engine (115 kW)  𝑇_𝑔𝑎𝑧 ∈ [400,800] °C
𝑃_𝑒𝑣 ∈[1,20] bar & 𝑤 ∈[0,20] g/s
Fully instrumented (t°, P, flows, power, internal pressure…)
Electricity generation from scroll expander to the battery

## Slide 5: Table of content Introduction
Introduction
Pump
Conclusions and prospects
Heat exchangers
Expander

## Slide 6: Evaporator Description
Spiral counter-flow evaporator characteristics
Evaporator efficiency: pressure drop and pinch point into account
Parameter | Value
Mass | 3.7 kg
Volume | 2.34 dm3
Water exchange area | 0.708 m2
Compacity | 302.6 m2/m3

## Slide 7: Evaporator Performance
Rather constant efficiency
High pressure drop on the water side

## Slide 8: Table of content Pump
Introduction
Pump
Conclusions and prospects
Heat exchangers
Expander

## Slide 9: Pump Description
Gear pump characteristics
Volumetric efficiency and isentropic efficiency
Parameter | Value
Swept volume | 0.5 cm3
Max. pressure | 20 bar
Max. mass flow (3000 RPM) | 20 g/s
Max. power consumption | 105 W

## Slide 10: Pump Performance
Maximum isentropic efficiency = 45%
Maximum volumetric efficiency = 90%

## Slide 11: Table of content Expander
Introduction
Pump
Conclusions and prospects
Heat exchangers
Expander

## Slide 12: Expander Description
Hermetic oil-free scroll expander
Taylor-made with a deterministic model of scroll
  Pockets of fluid, leakages, friction
Optimization of the geometry based on a normalized cycle
Parameter | Value
Swept volume | 8 cm3
Max. rotational speed | 15 000 RPM
Max. temperature | 250°C
Pressure | Up to 20 bars

## Slide 13: Expander Performance
Hermetic oil-free scroll expander
Isentropic efficiency and Filling factor
V1 and V2 (20% reduced lateral clearance)
Electrical power ~ 1kW

## Slide 14: Global Performance
Pump
65 W
= 35%
Evaporator
15000 W
Expander
950 W
= 25%
Efficiency=5.9%
Net power = 885 W
> 600W

## Slide 15: Table of content Expander
Introduction
Pump
Conclusions and prospects
Heat exchangers
Expander

## Slide 16: Conclusion
Experimental investigation
  Volumetric gear pump
  Taylor-made scroll expander
  Evaporator
Evaluation of the performance
  Rankine cycle steady-state model calibrated based on the experimentation
  Possibility of CO2 emissions reduction of 6.7 g/km
  Reduction of BSFC (Brake Specific Fuel Consumption) up to 5%
Perspectives
  Fluids : water mixture with ethanol
  Layout: cooling engine + R245fa
  Scroll V3 + turbine

## Slide 17: Conclusion
Thank you for your attention!
Olivier.dumont@ulg.ac.be