## Slide 1: Monitoring the ionosphere using new GNSS
R. Warnant1, C. Deprez1, G. Wautelet2, L. Van de Vyvere3
1University of Liege, Liege, Belgium.
2GRGS, Toulouse, France.
3M3 System, Wavre, Belgium.
International Beacon Satellite Symposium 2016
27 June - 1 July 2016, Trieste (Italy).

## Slide 2: Monitoring TEC for geodetic applications
For the last 25 years, TEC has been reconstructed from GPS L1/L2 code and phase pseudoranges in order to correct ionospheric effects on positioning applications.
  Absolute positioning is influenced by absolute TEC and “regular” gradients.
  Differential and relative positioning are influenced by regular gradients and also local variability in TEC (the latter mainly degrading precise applications).
GPS-based TEC monitoring data suffers from different shortcomings.

## Slide 3: Present shortcomings 1
Absolute TEC accuracy is limited to 2-5 TECU:
  Depends on code and phase pseudoranges precision.
  The use of code levelling to compute phase ambiguities degrades TEC accuracy due to low code precision (main limitation).
Limited spatial resolution:
  Depends on the number of satellites in view.
  In Liege, the number of GPS satellites in view ranges from 8 to 15 (average 11).
  A proper modeling of local variability in TEC requires increased spatial resolution.

## Slide 4: Present shortcomings 2
Monitoring of local variability in TEC at European mid-latitudes (Belgium):
  Mainly due Travelling Ionospheric Disturbances.
  Also detected during geomagnetic storms.
  Depends on phase pseudorange precision.
  Requires good spatial resolution.
  The detection of moving structures (TIDs) is « biased » by the fact that ionospheric points have a velocity wrt the ionosphere due to satellite orbital motion.

## Slide 5: New/modernized GNSS 1
GPS
GLONASS
Galileo
QZSS
Beidou
NAVIC
SBAS

## Slide 6: New/modernized GNSS 2
More (than 2) frequencies:
  Possible to form several frequency pairs to reconstruct TEC
  Development of improved ambiguity computation (even resolution ?) techniques.
Improved signals :
  Better resistance to multipath
  New modulation techniques allowing to perform more precise code pseudorange measurements.
More satellites:
  The combined use of al the available GNSS provides better redundancy and improved spatial resolution.

## Slide 7: New/modernized GNSS 3
Number of GNSS satellites in view (up to 40) in Liege (Belgium)

## Slide 8: New/modernized GNSS 4
Different types of orbits:
  Medium Earth Orbits (MEO)
  Geostationary Orbits (GEO)
  Inclined Geosynchronous Orbits (IGSO)
GEO orbits have a negligible velocity wrt respect to the ionosphere.
Therefore, GEO satellites have a particular interest for the study of local variability in TEC.

## Slide 9: Multi GNSS/multi-frequency TEC precision

## Slide 10: GNSS equipment
Located in Liege (Belgium).
2 Trimble GNSS choke ring antenna’s on a short baseline (5,352 m).
6 multi-GNSS/multi-frequency receivers :
  2 Trimble NetR9 receivers
  2 Septentrio PolaRx4 receivers
  1 Septentrio PolaRxS scintillation receiver
  1 Septentrio PolaRx5 (new model).
Equipment used to perform zero and short baseline tests for positioning and ionosphere monitoring.

## Slide 11: GNSS signals : GPS
L5
L2
L1

## Slide 12: GNSS signals : Galileo
E1
E6
E5b
E5
E5a
Only available with PolaRx5

## Slide 13: GNSS signals : Beidou
B2
B3
B1
Only available on NetR9 and PolaRx5

## Slide 14: Multi-GNSS/frequency TEC precision 1
For satellite “i” and receiver “p”, the code geometry free (GF) combination between frequency fk and fl :
Codes at frequency
fk and fl
InterFrequency
rec. and
sat. biases
Slant TEC
Multipath
Noise

## Slide 15: Multi-GNSS/frequency TEC precision 2
Reconstructed TEC precision mainly depends on :
  Code pseudorange (Pk,Pl) precision.
  Multipath.
  IF biases variability (one usually assume that they are stable over short time periods).
  The “TEC coefficient” :
Same demonstration can be done for phase pseudoranges which contain an additional term: the phase ambiguity.

## Slide 16: Multi-GNSS/frequency TEC precision 3
Given the same code precision, a larger frequency difference gives a smaller TEC coefficient and therefore a better TEC precision.
TEC coefficients |  |  |  |  |  |  |  | 
Galileo |  |  |  | GPS |  |  | Beidou | 
E1-E5a | E1-E5b | E1-E5 | E1-E6 | L1-L2 | L1-L5 | L2-L5 | B1-B2 | B1-B3
7,764 | 8,757 | 8,24 | 11,893 | 9,52 | 7,764 | 42,089 | 8,993 | 11,754

## Slide 17: Multi-GNSS/frequency TEC precision 4
Code pseudorange precision (large differences between frequencies/receivers !)

## Slide 18: Multi-GNSS/frequency TEC precision 5
Phase pseudorange precision: small differences between frequencies/receivers

## Slide 19: Methodology to asses TEC precision 1
Compute Slant TEC change from epoch to epoch (30 s interval) without normalization:
  Removes biases (constant part of IF delays, ambiguities)
  Still depends on noise and on between epoch variation of TEC and multipath
Form single (between receiver) differences of on ULg short baseline (5,352 m):
  Completely removes TEC (same ionosphere).
  Still contains multipath and noise.

## Slide 20: Methodology to asses TEC precision 2
TEC precision is estimated by computing the standard deviation of single differences of and by dividing them by 2 (error propagation).

## Slide 21: Results: code (multipath filter off - mask 10°)
Chart: Code TEC precision (TECU)
| E1-E5a | E1-E5b | E1-E5 | L1-L2 | L1-L5 | B1-B2 | B1-B3 | Galileo | GPS | Beidou MEO
Septentrio | 1.642 | 1.829 | 1.401 | 2.424 | 2.105 | 3.423
Trimble | 2.363 | 2.762 | 2.074 | 4.951 | 3.909 | 4.342 | 5.363

## Slide 22: Results: Phase (multipath filter off - mask 10°)
Chart: Phase TEC precision (TECU)
| E1-E5a | E1-E5b | E1-E5 | L1-L2 | L1-L5 | B1-B2 | B1-B3 | Galileo | GPS | Beidou MEO
Septentrio | 0.012 | 0.013 | 0.011 | 0.012 | 0.011 | 0.014
Trimble | 0.008 | 0.009 | 0.008 | 0.017 | 0.01 | 0.013 | 0.0135

## Slide 23: Results: code (multipath filter on - mask 20°)
Chart: Septentrio Code TEC precision (TECU)
| E1-E5a | E1-E5b | E1-E5 | L1-L2 | L1-L5 | B1-B2 | B1-B3 | Galileo | GPS | Beidou MEO
Septentrio | 0.767 | 0.903 | 0.709 | 1.288 | 0.964 | 2.104

## Slide 24: Slant TEC Galileo E1-E5 code versus phase

## Slide 25: Multi-GNSS/frequency TEC: Summary 1
Strong improvement in code TEC precision with Galileo wrt the “standard” GPS L1/L2.
  Galileo E1/E5 combination has a precision better than 1 TECU above 20° elevation (Septentrio PolaRx4).
  This will bring improvement in code-phase leveling.
   Better TEC accuracy.
  Depending on application requirement, TEC could directly be obtained from code measurements.
     No phase ambiguity to compute
     No problem with cycle slips, in particular during disturbed ionosphere conditions.

## Slide 26: Multi-GNSS/frequency TEC: Summary 2
As far as phase TEC accuracy is concerned, for Septentrio receivers, TEC precision has similar accuracy levels of about 0,012 TECU (mask 10°) for the different combinations/GNSS.
For Trimble receivers, Galileo provides the best accuracy (0,008 TECU).

## Slide 27: GEO satellites for ionosphere monitoring

## Slide 28: GEO at European mid-latitude (Liège, Belgium)
C02
C05
GAGAN S127
EGNOS S123 and S136
Beidou
  C02 (1°-2°)
  C05 (15°)
SBAS
  GAGAN (India)
    S127 (16°)
  EGNOS (Europe)
    S123 (27°)
    S136 (32°)
NAVIC
  I06 (29°)
  Only single frequency available yet (with PolaRx5).

## Slide 29: Beidou GEO : Phase

## Slide 30: Beidou GEO : Code

## Slide 31: Beidou GEO: SD of (C05)

## Slide 32: Beidou GEO: accuracy
Chart: Beidou GEO Code TEC precision (TECU)
| B1-B2 | B1-B2 | C05 | C02
 | 3.849 | 7.641
Chart: Beidou Phase TEC precision (TECU)
| B1-B2 | B1-B2 | C05 | C02
 | 0.023 | 0.045

## Slide 33: Beidou GEO: Slant phase TEC

## Slide 34: Beidou GEO: Summary 1
In Liege (Belgium), Beidou GEO satellites C05 (15°) and C02 (1-2°) can be tracked by all Septentrio receivers.
C05 data are continuous (in average less than 1 cycle slip a day).
   Phase ambiguity often remains the same during several days.
C02 data are usually continuous during several hours (up to 24 hours).
Given phase TEC accuracy (C05: 0,023 TECU) and (C02: 0,045 TECU), both satellites could be used to monitor TEC or local variability in TEC.

## Slide 35: Beidou GEO: Summary 2
Code leveling could be degraded by code noise but ambiguities are usually computed on much longer time periods.
Further investigations are necessary to interpret the variability observed in
  Multipath, Ionosphere, variability in IF biases.
Our Trimble NetR9 receivers only track C05 but data are unusable due to cycle slips.

## Slide 36: Thanks for your attention !