## Slide 1: Master’s dissertation
Student:
Gilles CORMAN
“Formulation of a macro-element for suction caisson foundations under axial tensile load”
Student: | Supervisors: |  | 8th of December, 2017
Gilles CORMAN | Prof. A. BEZUIJEN | UGent | 
 | Prof. F. COLLIN | University of Liège | 
 | B. CERFONTAINE | University of Liège | 

## Slide 2
Context
CORMAN Gilles
Master Thesis
December 2017
Need for renewable energy
Onshore vs Offshore
Variants for OWT foundations
Suction Caissons
REN 21, 2015
Schaumann P et al, 2011
EWEA, 2017
Introduction
  Context
  Suction caissons
Description of the FE model
Drained simulations
Partly drained simulations
Conclusion

## Slide 3
Suction caissons
CORMAN Gilles
Master Thesis
December 2017
Foundation system for OWT’s
Hollow steel cylinder open towards the bottom
Monopod or tetra/tri-pod superstructure
Two-step installation by pressure differential
Cheaply, silently and quickly installed, reusable
Houlsby et al. 2005
Introduction
  Context
  Suction caissons
Description of the FE model
Drained simulations
Partly drained simulations
Conclusion

## Slide 4
Problem statement
CORMAN Gilles
Master Thesis
December 2017
Introduction
Description of the FE model
  Problem statement
  Geometry
  Interface elements
  Initial loading state
  Case studies
Drained simulations
Partly drained simulations
Conclusion
One single caisson
Part of a tripod
Uniaxial tensile load
2D axisymmetric
Displacement imposed
Houlsby et al. 2005
Use of rheological elements
Approximation of the stiffness

## Slide 5
Geometry
CORMAN Gilles
Master Thesis
December 2017
Size | Diameter |  |  | 8m | 
 | Skirt length |  |  | 8m | 
 | Thickness |  |  | 0.1m | %
Water depth |  |  |  | 20m | 
Linear elastic soil and caisson |  |  |  |  | 
Lateral earth pressure coefficient at rest |  |  |  | 1 | 
Porosity |  |  |  | 0.5 | 
Boundary conditions |  |  |  |  | 
Mechanical |  |  |  |  | 
Hydraulic |  | Permeable |  |  | 
 |  | Impermeable |  |  | 
Size | Diameter |  |  | 8m | 
 | Skirt length |  |  | 8m | 
 | Thickness |  |  | 0.1m | 
Water depth |  |  |  | 20m | 
Linear elastic soil and caisson |  |  |  |  | 
Lateral earth pressure coefficient at rest |  |  |  | 1 | 
Porosity |  |  |  | 0.5 | 
Boundary conditions |  |  |  |  | 
Mechanical |  |  |  |  | 
Hydraulic |  | Permeable |  |  | 
 |  | Impermeable |  |  | 
Introduction
Description of the FE model
  Problem statement
  Geometry
  Interface elements
  Initial loading state
  Case studies
Drained simulations
Partly drained simulations
Conclusion

## Slide 6
Interface elements
CORMAN Gilles
Master Thesis
December 2017
Permeability |  |  | 
Transmissivity |  |  | 
Permeability |  |  | 
Transmissivity |  |  | 
Mechanical behaviour
Coulomb dry friction law
Flow behaviour
Friction coefficient |  | 0.5 | [-]
Penalty coefficients |  |  | 
Friction coefficient |  | 0.5 | [-]
Penalty coefficients |  |  | 
Hydro-mechanical couplings
Introduction
Description of the FE model
  Problem statement
  Geometry
  Interface elements
  Initial loading state
  Case studies
Drained simulations
Partly drained simulations
Conclusion

## Slide 7
Initial loading state
CORMAN Gilles
Master Thesis
December 2017
Identification of components of reaction
1. |  |  | Downward
2. | Water weight |  | 
3a. & 3b. | Friction |  | 
4. | Pore water pressure |  | 
5. | Weight of the soil plug |  | 
6a. & 6b. | Buoyancy force |  | Upward
7a. & 7b. | Soil pressure |  | 
8. | Total reaction |  | 
1. |  |  | Downward
2. | Water weight |  | 
3a. & 3b. | Friction |  | 
4. | Pore water pressure |  | 
5. | Weight of the soil plug |  | 
6a. & 6b. | Buoyancy force |  | Upward
7a. & 7b. | Soil pressure |  | 
8. | Total reaction |  | 
Caisson weight
State of equilibrium
Introduction
Description of the FE model
  Problem statement
  Geometry
  Interface elements
  Initial loading state
  Case studies
Drained simulations
Partly drained simulations
Conclusion

## Slide 8
Case studies
CORMAN Gilles
Master Thesis
December 2017
Scenario | Sub-case | Drainage condition | Soil condition
1 | 1-1 | Drained | Rigid body motion
 | 2-2 | Drained | Free to move
2 | 3 | Partly drained | Rigid body motion
 | 4 | Partly drained | Free to move
Scenario | Sub-case | Drainage condition | Soil condition
1 |  | Drained | Rigid body motion
 |  | Drained | Free to move
2 | 3 | Partly drained | Rigid body motion
 | 4 | Partly drained | Free to move
Simulations
Reference parameters
Elastic modulus |  | 
Poisson’s ratio |  | 
Tangential penalty coeff. |  | 
Permeability |  | 
Loading rate |  | 
Elastic modulus |  | 
Poisson’s ratio |  | 
Tangential penalty coeff. |  | 
Permeability |  | 
Loading rate |  | 
Introduction
Description of the FE model
  Problem statement
  Geometry
  Interface elements
  Initial loading state
  Case studies
Drained simulations
Partly drained simulations
Conclusion

## Slide 9
Reaction modes
CORMAN Gilles
Master Thesis
December 2017
Introduction
Description of the FE model
Drained simulations
  Reaction modes
  Numerical-Analytical
  Macro-element
Partly drained simulations
Conclusion
Rigid body motion
Soil free to move
[1a] [2a]
[1b] [2b]

## Slide 10
Reaction modes (2)
CORMAN Gilles
Master Thesis
December 2017
Rigid body motion
Soil free to move
Introduction
Description of the FE model
Drained simulations
  Reaction modes
  Numerical-Analytical
  Macro-element
Partly drained simulations
Conclusion

## Slide 11
Numerical vs Analytical
CORMAN Gilles
Master Thesis
December 2017
Rigid body motion
Integration of the shear distribution
Friction components [1a & 2a]
Introduction
Description of the FE model
Drained simulations
  Reaction modes
  Numerical-Analytical
  Macro-element
Partly drained simulations
Conclusion

## Slide 12
Numerical vs Analytical (2)
CORMAN Gilles
Master Thesis
December 2017
Soil free to move
Expression for given in the literature
where
Friction components [1b & 2b]
Randolph & Wroth, 1978
Introduction
Description of the FE model
Drained simulations
  Reaction modes
  Numerical-Analytical
  Macro-element
Partly drained simulations
Conclusion

## Slide 13
Macro-Element
CORMAN Gilles
Master Thesis
December 2017
Soil free to move
[1b & 2b]
=
=
Introduction
Description of the FE model
Drained simulations
  Reaction modes
  Numerical-Analytical
  Macro-element
Partly drained simulations
Conclusion
=
Rigid body motion
[1a & 2a]

## Slide 14
Reaction modes
CORMAN Gilles
Master Thesis
December 2017
Rigid body motion
Soil free to move
Introduction
Description of the FE model
Drained simulations
Partly drained simulations
  Reaction modes
  Numerical-Analytical
  Macro-element
Conclusion
[1a] [2a] [3a]
[1b] [2b] [3b] [4b]

## Slide 15
Reaction modes (2)
CORMAN Gilles
Master Thesis
December 2017
Rigid body motion
Soil free to move
Introduction
Description of the FE model
Drained simulations
Partly drained simulations
  Reaction modes
  Numerical-Analytical
  Macro-element
Conclusion

## Slide 16
Reaction modes (3)
CORMAN Gilles
Master Thesis
December 2017
Rigid body motion
Soil free to move
Introduction
Description of the FE model
Drained simulations
Partly drained simulations
  Reaction modes
  Numerical-Analytical
  Macro-element
Conclusion

## Slide 17
Numerical vs Analytical
CORMAN Gilles
Master Thesis
December 2017
Rigid body motion
Friction components [1a & 2a]
PWP component [3a]
Similar to the drained simulation
Darcy’s law
Hydraulic gradient
Seepage length
Senders M. & Randolph M.F, 2009
Introduction
Description of the FE model
Drained simulations
Partly drained simulations
  Reaction modes
  Numerical-Analytical
  Macro-element
Conclusion

## Slide 18
Numerical vs Analytical (2)
CORMAN Gilles
Master Thesis
December 2017
Soil free to move
Outer friction component [1b]
Expression for similar to the drained simulation
where
where
Introduction
Description of the FE model
Drained simulations
Partly drained simulations
  Reaction modes
  Numerical-Analytical
  Macro-element
Conclusion

## Slide 19
Numerical vs Analytical (3)
CORMAN Gilles
Master Thesis
December 2017
Soil free to move
Inner friction component [2b]
Expression for similar to the drained simulation
where
Linear reduction due to plug uplift
Senders M, 2008
Introduction
Description of the FE model
Drained simulations
Partly drained simulations
  Reaction modes
  Numerical-Analytical
  Macro-element
Conclusion

## Slide 20
Numerical vs Analytical (4)
CORMAN Gilles
Master Thesis
December 2017
Soil free to move
PWP component [3b]
Darcy’s law
Hydraulic gradient
Seepage length
Senders M. & Randolph M.F, 2009
Introduction
Description of the FE model
Drained simulations
Partly drained simulations
  Reaction modes
  Numerical-Analytical
  Macro-element
Conclusion

## Slide 21
Numerical vs Analytical (5)
CORMAN Gilles
Master Thesis
December 2017
Soil free to move
Plug uplift component [4b]
Principle of the mechanical work :
Generated work during :
Iterative process
Romp R.H, 2013
Introduction
Description of the FE model
Drained simulations
Partly drained simulations
  Reaction modes
  Numerical-Analytical
  Macro-element
Conclusion

## Slide 22
Macro-element Rigid body motion
CORMAN Gilles
Master Thesis
December 2017
Friction component
[1a & 2a]
PWP component
[3a]
Introduction
Description of the FE model
Drained simulations
Partly drained simulations
  Reaction modes
  Numerical-Analytical
  Macro-element
Conclusion

## Slide 23
Macro-element Soil free to move
CORMAN Gilles
Master Thesis
December 2017
Friction components
[1b & 2b]
PWP component
[3b]
Plug component
[4b]
Introduction
Description of the FE model
Drained simulations
Partly drained simulations
  Reaction modes
  Numerical-Analytical
  Macro-element
Conclusion

## Slide 24
Conclusion
CORMAN Gilles
Master Thesis
December 2017
Introduction
Description of the FE model
Drained simulations
Partly drained simulations
Conclusion
Scenario | Sub-case | Drainage condition | Soil condition | Resistance
1 | 1-1 | Drained | Rigid body motion | 
 | 2-2 | Drained | Free to move | 
2 | 3 | Partly drained | Rigid body motion | 
 | 4 | Partly drained | Free to move | 
Scenario | Sub-case | Drainage condition | Soil condition | Resistance
1 |  | Drained | Rigid body motion | 
 |  | Drained | Free to move | 
2 | 3 | Partly drained | Rigid body motion | 
 | 4 | Partly drained | Free to move | 

## Slide 25: Thank you for your attention
Notes: As you may know, the main purpose of this assignment is to design an artificial island and harbour in the north sea.