## Slide 1: EQUINE SEMEN FREEZING
Jérôme PONTHIER, ULg
DVM, M. Sc., Ph. D., Diplomate ECAR

## Slide 2: Plan
Aims
Procedures
Future

## Slide 3: 1. Aims
>50% pregnant mares after AI
  AI timing & procedures?
    Depending on the author
  See Vidament et al.2005
140x106 prog spermatozoa per dose
  >35% prog motility
  400x106 total spz
  4 to 8 straws, 2 to 4ml (200 to 100x106spz/ml)
WBSHF: 250x106 prog spermatozoa per dose
  Scientific data about it = ?

## Slide 4: 2. Procedure
Extender 1
Extender 2:
With cryoprotective agent
Dilution 1
Dilution 2
Centrifugation
Cooling
4°C
Freezing
straws
Filtration
Gel
-140°C
-196°C

## Slide 5: 2. Procedure
First dilution
  Skim Milk or Skim Milk related medium
    e.g.: INRA 96TM (used for fresh semen dilution)
  Aims:
    Working at 20°C
    Nutrition of spz during manipulation & centrifugation
    Typically: 50% of semen - 50% of extender

## Slide 6: 2. Procedure
Centrifugation
  Aims:
    Replacement of seminal plasma by freezing extender
    Recovery of maximum nbr of spz
  Protocols:
    Classical:
      600xg 10 minutes, RR=60-70%
    Cushionned medium:
      1000xg 20 minutes, RR=85-95%
      Ioxidanol solution

## Slide 7: 2. Procedure
Second Dilution
  Choosing second dilution extender:
    INRA82®, Ghent®, Botucryo®, Inra Freeze®,…
    Differences in cryoprotective agents:
      Glycerol, amides, others…
      Different concentrations (glycerol toxicity…)
    Side agents: egg yolk, LDL, cholesterol,…
  Aim of the step: add freezing extender volume:
    To obtain the good spz concentration
    To respect minimal cryoprotective agent concentration

## Slide 8: 2. Procedure
Second Dilution
  Choosing concentration in straws
Pellet without cryo agent
Extender with cryo agent
Extender with cryo agent
Final [cryo agent]: 3.4%
Final [cryo agent]: 2.9%
Low []
High []

## Slide 9: 2. Procedure
Second Dilution
  Adding the good extender volume to the pellet
    TSNfresh=[ ]fresh x volfresh
    TSNest post centri = [ ]fresh x volfresh x RRest
      Typically: 0.7 or 0.9
    Volest of extender to add=
      TSNest post centri/[ ]straws
        But ESTIMATION:
        Add ½ volest and:
        TSNreal PC = [ ]PC x volest/2
        Volreal=TSNreal PC/[ ]straws

## Slide 10: 2. Procedure
Cooling
  Min: 90 minutes (positive effect if time is increased in some papers)
Straw filling
  Equine straws= 0.5ml
  Mechanical
Freezing
  -40 - -60°C/min
  >-140°C
Storage in N2
  -196°C

## Slide 11: 3. Future
Spermatozoa sorting
  By quality: density gradient centrifugation:
  Selection of motile & normal spz on the basis of the isopicnotic point before freezing
  Filtration of: abnormal spz, spz with fragmented DNA, non-sperm cells, cellular debris, bacteria, EVA (?)
  Loss of spermatozoa!! (RR: 10-40%)

## Slide 12: 3. Future
Spermatozoa sorting
  By sex:
    Sexing technologies: DNA content measure by flow cytometry-like device & sorting
    Currently in equine: after sorting, spz doesn’t stand freezing
    To be continued…

## Slide 13: 3. Future
Freezability prognosis
  In the human:
    Membrane fluidity
    GSH concentration & GPX transcription
    Membrane integrity & symetry: Annexin V
  In the equine:
    Apoptotic factors (by flow cytometry)
    NSCs?

## Slide 14: 3. Future
Freezing extender improvement
  Cryoprotective agents
    Reducing glycerol concentration (3.5% > 2.5% > 0.5%)
    Lipids and Amides cryoprotective effects to replace glycerol (Botucryo®)
  Physicochemicals and nutritive characteristics
    Cholesterol
    Isolation of LDL (INRA Freeze®)
    Animal protein free media
  Control of ROS production by medium
  Decrease nbr of straws/dose (decrease of secondary market)

## Slide 15: 3. Future
Technical improvement
  Cooling?
    After centrifugation
    Time can be increased
  Freezing?
    Curves?
    Vitrification
Real
Theorical
T°C
Time

## Slide 16: EqSemenFreezing: MQC1
Which of the following batches of this same stallion would be suitable for export in 8 straws dose?
 | Concentration (x106/ml) | Total Motility (%) | Progressive Motility (%)
Batch 1 | 100 | 50 | 25
Batch 2 | 200 | 40 | 10
Batch 3 | 100 | 40 | 35
Batch 4 | 200 | 35 | 15

## Slide 17: EqSemenFreezing: MQC1
Which of the following batches of this same stallion would be suitable for export in 8 straws dose?
 | Concentration (x106/ml) | Total Motility (%) | Progressive Motility (%)
Batch 1 | 100 | 50 | 25
Batch 2 | 200 | 40 | 10
Batch 3 | 100 | 40 | 35
Batch 4 | 200 | 35 | 15

## Slide 18: EqSemenFreezing: MQC2
Rational of the use of cushioned centrifugation during equine semen freezing is:
To decrease spermatozoa lesions
To increase recovery rate
To increase spermatozoa progessive motility
To decrease spermatozoa abnormalities

## Slide 19: EqSemenFreezing: MQC2
Rational of the use of cushioned centrifugation during equine semen freezing is:
To decrease spermatozoa lesions
To increase recovery rate
To increase spermatozoa progessive motility
To decrease spermatozoa abnormalities