## Slide 1: Feasibility study of low-carbon ammonia and steel production in Europe
Jean-Luc Hoxha
Marc Philippart de Foy
17th September 2020
Notes: CHANGER ET METTRE LES BONS LOGOS

## Slide 2: Introduction
Objective of the study:
Feasibility study of low-carbon ammonia and steel production in Europe
  J-L. Hoxha, M. Caspar, A. Donceel, J. Fraselle, G. Léonard, M. Philippart de Foy, R. Poncelet
  ECEEE Industrial Efficiency Decarbonise Industry - 14-17 September 2020 - Digital Event
Feasibility of decarbonised production of ammonia and steel in 2030
What are the required assumptions to reach that goal?
European Union: carbon neutral by 2050 [1]
→ H2 produced by water electrolysis from renewable electricity
→ Modelling with Aspen Plus and cost analysis based on Turton et al. [2]

## Slide 3
Plan
Feasibility study of low-carbon ammonia and steel production in Europe
  J-L. Hoxha, M. Caspar, A. Donceel, J. Fraselle, G. Léonard, M. Philippart de Foy, R. Poncelet
  ECEEE Industrial Efficiency Decarbonise Industry - 14-17 September 2020 - Digital Event
Proton exchange membrane electrolyser
Introduction
Ammonia production
Steelmaking
Cost analysis
Conclusion

## Slide 4: Proton Exchange Membrane (PEM) Electrolyser
Criteria for the choice of the electrolyser:
Feasibility study of low-carbon ammonia and steel production in Europe
  J-L. Hoxha, M. Caspar, A. Donceel, J. Fraselle, G. Léonard, M. Philippart de Foy, R. Poncelet
  ECEEE Industrial Efficiency Decarbonise Industry - 14-17 September 2020 - Digital Event
- Flexible for a fluctuating electricity supply
- Able to operate under high pressure: 200 bar max
- Assumed efficiency of 85% in 2030 [3]

## Slide 5: Ammonia production
Common plants:
→ 2 tCO2/tNH3
Natural gas reforming
(CO + H2)
Air
(source of N2)
Reactor
3 H2 + N2 → 2 NH3
Separation
Outlets
Unreacted H2 and N2
Water electrolysis
(O2 + H2)
Pure liquid N2
Reactor
3 H2 + N2 → 2 NH3
Separation
Outlets
Unreacted H2 and N2
Feasibility study of low-carbon ammonia and steel production in Europe
  J-L. Hoxha, M. Caspar, A. Donceel, J. Fraselle, G. Léonard, M. Philippart de Foy, R. Poncelet
  ECEEE Industrial Efficiency Decarbonise Industry - 14-17 September 2020 - Digital Event
Decarbonised plant:
→ 0 tCO2/tNH3
5

## Slide 6: Ammonia production
Feasibility study of low-carbon ammonia and steel production in Europe
  J-L. Hoxha, M. Caspar, A. Donceel, J. Fraselle, G. Léonard, M. Philippart de Foy, R. Poncelet
  ECEEE Industrial Efficiency Decarbonise Industry - 14-17 September 2020 - Digital Event

## Slide 7: Steelmaking – Direct reduction iron (DRI)
Common DRI plants*:
→ 0.5 tCO2/tsteel
iron ore
unreacted CO +H2
heating
reduction
electric arc furnace (EAF)
steel
fumes
slag
natural gas reforming
(CO + H2)
reducing gas
(CO > H2)
iron ore
unreacted CO +H2
heating
reduction
electric arc furnace (EAF)
reducing gas
(H2 > CO)
water electrolysis
(O2 + H2)
small CO injection
steel
fumes
slag
Common steelmaking plants: → 2 tCO2/tsteel
*DRI = 5% of the world’s steel production (BAT)
Decarbonised plant:
→ 0.15 tCO2/tsteel
7
cooling
deeper reduction
carbon, oxygen
limestone, scrap
carbon, oxygen
limestone, scrap

## Slide 8: Steelmaking
Feasibility study of low-carbon ammonia and steel production in Europe
  J-L. Hoxha, M. Caspar, A. Donceel, J. Fraselle, G. Léonard, M. Philippart de Foy, R. Poncelet
  ECEEE Industrial Efficiency Decarbonise Industry - 14-17 September 2020 - Digital Event
8

## Slide 9: Cost analysis
Reminder of the objective:
Feasibility study of low-carbon ammonia and steel production in Europe
  J-L. Hoxha, M. Caspar, A. Donceel, J. Fraselle, G. Léonard, M. Philippart de Foy, R. Poncelet
  ECEEE Industrial Efficiency Decarbonise Industry - 14-17 September 2020 - Digital Event
Main variables influencing the cost:
- CAPEX (Turton et al [2])
- Electricity price
- CO2 taxes
- Product prices
- Raw material prices
Construction of a new decarbonised grass-roots plant operating 8200 h/yr
Notes: Prix de l’electircité qui s’applique de facon similaire aux deux procédés.
Le prix des matières premieres sont des variables fixées en fonction de la littérature et des données récentes.

## Slide 10: Cost analysis - electricity price
Classic ammonia plant: 100 GWh/yr [4]
Feasibility study of low-carbon ammonia and steel production in Europe
  J-L. Hoxha, M. Caspar, A. Donceel, J. Fraselle, G. Léonard, M. Philippart de Foy, R. Poncelet
  ECEEE Industrial Efficiency Decarbonise Industry - 14-17 September 2020 - Digital Event
Peak shaving approach:
Can expect a decrease of 25 to 35%
→ Electricity price of 30 €/MWh
Decarbonised ammonia plant: 5000 GWh/yr
→ Normal electricity price of 40 €/MWh

## Slide 11: Cost analysis – Ammonia production
Sensitivity study on CO2 taxes:
→ For an electricity cost of 30 €/MWh: 225 €/tCO2
profitable
not profitable
Discounted cash flow diagram
CO2 taxes = 250 €/tCO2
electricity price = 30 €/MWh
discount rate = 10%
ammonia price = 350 €/tNH3
Feasibility study of low-carbon ammonia and steel production in Europe
  J-L. Hoxha, M. Caspar, A. Donceel, J. Fraselle, G. Léonard, M. Philippart de Foy, R. Poncelet
  ECEEE Industrial Efficiency Decarbonise Industry - 14-17 September 2020 - Digital Event
Notes: Fictious income compared to other classic plants.

## Slide 12: Cost analysis - Steelmaking
Sensitivity study on steel price:
→ For an electricity cost of 30 €/MWh: 635 €/tsteel
Discounted cash flow diagram
CO2 taxes = 0 €/tCO2
electricity price = 30 €/MWh
discount rate = 10%
steel price = 840 €/tsteel
profitable
not profitable
Feasibility study of low-carbon ammonia and steel production in Europe
  J-L. Hoxha, M. Caspar, A. Donceel, J. Fraselle, G. Léonard, M. Philippart de Foy, R. Poncelet
  ECEEE Industrial Efficiency Decarbonise Industry - 14-17 September 2020 - Digital Event

## Slide 13: Conclusion
Feasibility study of low-carbon ammonia and steel production in Europe
  J-L. Hoxha, M. Caspar, A. Donceel, J. Fraselle, G. Léonard, M. Philippart de Foy, R. Poncelet
  ECEEE Industrial Efficiency Decarbonise Industry - 14-17 September 2020 - Digital Event
Assumptions to obtain an economically viable processes:
- Maturity of PEM electrolysers at 85% efficiency
- Electricity price can be negotiated (peak shaving)
- Fully renewable electricity supply (currently unrealistic)
Ammonia large increase of CO2 taxes
Steelmaking high price of steel
13
Notes: Parler des taxes CO2 en hollande et du projet européen 60%.

## Slide 14: References
[1] European Commission, Rapport de la commission : Quatrième rapportsur l’état de l’union de l’énergie, 2019.
[2] R. Turton R. Bailie W. Whiting J. Shaeiwitz, D. Bhattacharyya. Analysis, Synthesis, and Design of Chemical Processes. Pearson, 2013.
[3] L. Cronin G. Chisholm. Hydrogen From Water Electrolysis, chapter ,pages 315–343. School of Chemistry, University of Glasgow, Glasgow, 2016.
[4] Schrefler F. Genoese A. Marcu A. Renda J. Wieczorkiewicz S. Roth F. Infelise G. Luchetta L. Colantoni W. Stoefs J. Timini F. Simonelli C. Egenhofer, V. Rizos. Composition and drivers of energy prices andcosts in energy intensive industries: the case of ceramics, flat glass and chemical industries. Center For European Policy Studies, 2014.
Feasibility study of low-carbon ammonia and steel production in Europe
  J-L. Hoxha, M. Caspar, A. Donceel, J. Fraselle, G. Léonard, M. Philippart de Foy, R. Poncelet
  ECEEE Industrial Efficiency Decarbonise Industry - 14-17 September 2020 - Digital Event
14

## Slide 15: THANK YOU FOR YOUR ATTENTION Any questions ?
Feasibility study of low-carbon ammonia and steel production in Europe
  J-L. Hoxha, M. Caspar, A. Donceel, J. Fraselle, G. Léonard, M. Philippart de Foy, R. Poncelet
  ECEEE Industrial Efficiency Decarbonise Industry - 14-17 September 2020 - Digital Event