## Slide 1: EURAD PhD Event N°1
Webinar, 15th of September 2020
Gilles Corman 1
1 University of Liège – UEE Research Unit
Hangbiao Song 1
Notes: Front page

## Slide 2: About me
Background
Belgian PhD student
University of Liège, Belgium
Geomechanics and Engineering Geology team
Thesis question:
Involvement in the project
EURAD WockPackage 6 GAS
Task 2 – SubTask 2.2: Advection: conceptualisation of the gas transport mechanisms at micro and macro scales
Task 3 – SubTask 3.3: Evaluate achievements by model-supported data analyses: predictive modelling and
application of newly developed modelling tool on in situ experiments
« Can the gas overpressure generation lead to the (re)fracturing of the rock and the creation of preferential flow pathways? »
1
Notes: Within task 2, we planned to focus especially on the subtask 2.2, dedicated to advection, with the aim of conceptualizing the gas transport mechanisms at micro and macro scales.
To that end, we are interested:
- on the one hand in gas transfers through the excavation damaged zone
on the other hand in gas migrations in the sound rock layers
For those who wants to now exactely where Liège, where we did the first annual meeting

## Slide 3: About my research
Figure: Supercontainer reference design,
adapted from [2].
Host rock
Main gallery
Storage alveole
Figure: Conceptual scheme of a deep geological disposal,
adapted from [1].
Zone I:
gas transfers through the EDZ
Zone II:
gas transfers in the sound rock layers
Controlled by the hydraulic properties modifications induced by fracturation
Governed by the rock structure at a micro-level
2
Notes: Within task 2, we planned to focus especially on the subtask 2.2, dedicated to advection, with the aim of conceptualizing the gas transport mechanisms at micro and macro scales.
To that end, we are interested:
- on the one hand in gas transfers through the excavation damaged zone
on the other hand in gas migrations in the sound rock layers
For those who wants to now exactely where Liège, where we did the first annual meeting

## Slide 4: About my research
In the EDZ:
Development of a second gradient H²M model to reproduce the rock environment around the deep geological disposal
A multiphysics porous medium [3]
3 species:
Distributed in 3 phases:
Solid phase
Liquid phase
Gas phase
Mineral species
Water species
Air species
Dissolved air
Dry air
Liquid water
Water vapour
Multiphysical couplings:
3
Notes: So far, our work focussed on the modelling of gas transfers in the EDZ.
The first objective was to develop a numerical model capable of reproducing the argillaceous rock environment surrounding the deep geological disposal. It can first be considered as a multiphysics porous medium. Moreover to properly model the localisation processes characterizing this zone, we have rather recourse to a model of second gradient type. And finally, a permeability evolution with strain has also been integrated into the model.
This model is currently operational
The second objective was to applied the developed model to the case of a large-scale gallery. At the present time, we have reached the final stage of these simulations, by performing a sensitivity study to highlight the effect of permeability variations, the effect of variations of H2 entry pressure or the influence of the type of gas relative permeability formulation
The last part of this task is to present and publish the results to the scientific community. The writing of an article is under process while the presentation of the results had to be postponed due to the crisis. This last point appears to be the only noticeable effect of the current situation on our work.

## Slide 5: About my research
In the EDZ:
Development of a second gradient H²M model to reproduce the rock environment around the deep geological disposal
A multiphysics porous medium [3]
With strain localisation [4]
elements
20 elements
Deviatoric strain
increment
Plastic loading index
Deviatoric strain increment
Plastic loading index
Classical FE method:
Mesh size dependency
Second gradient model = Regularisation technique
Shear band width control
No mesh size dependency
3
Notes: So far, our work focussed on the modelling of gas transfers in the EDZ.
The first objective was to develop a numerical model capable of reproducing the argillaceous rock environment surrounding the deep geological disposal. It can first be considered as a multiphysics porous medium. Moreover to properly model the localisation processes characterizing this zone, we have rather recourse to a model of second gradient type. And finally, a permeability evolution with strain has also been integrated into the model.
This model is currently operational
The second objective was to applied the developed model to the case of a large-scale gallery. At the present time, we have reached the final stage of these simulations, by performing a sensitivity study to highlight the effect of permeability variations, the effect of variations of H2 entry pressure or the influence of the type of gas relative permeability formulation
The last part of this task is to present and publish the results to the scientific community. The writing of an article is under process while the presentation of the results had to be postponed due to the crisis. This last point appears to be the only noticeable effect of the current situation on our work.

## Slide 6: About my research
In the EDZ:
Development of a second gradient H²M model to reproduce the rock environment around the deep geological disposal
A multiphysics porous medium [3]
With strain localisation [4]
Including transfer properties evolution with strain [5]
Parameter
Power cubic formulation
In situ fitting
3
Notes: So far, our work focussed on the modelling of gas transfers in the EDZ.
The first objective was to develop a numerical model capable of reproducing the argillaceous rock environment surrounding the deep geological disposal. It can first be considered as a multiphysics porous medium. Moreover to properly model the localisation processes characterizing this zone, we have rather recourse to a model of second gradient type. And finally, a permeability evolution with strain has also been integrated into the model.
This model is currently operational
The second objective was to applied the developed model to the case of a large-scale gallery. At the present time, we have reached the final stage of these simulations, by performing a sensitivity study to highlight the effect of permeability variations, the effect of variations of H2 entry pressure or the influence of the type of gas relative permeability formulation
The last part of this task is to present and publish the results to the scientific community. The writing of an article is under process while the presentation of the results had to be postponed due to the crisis. This last point appears to be the only noticeable effect of the current situation on our work.

## Slide 7: About my research
7m
7m
10.4m
Plastic loading index
In the EDZ:
Application to large-scale storage drift
1E-4
Deviatoric strain increment
Development of a second gradient H²M model to reproduce the rock environment around the deep geological disposal
3
Notes: So far, our work focussed on the modelling of gas transfers in the EDZ.
The first objective was to develop a numerical model capable of reproducing the argillaceous rock environment surrounding the deep geological disposal. It can first be considered as a multiphysics porous medium. Moreover to properly model the localisation processes characterizing this zone, we have rather recourse to a model of second gradient type. And finally, a permeability evolution with strain has also been integrated into the model.
This model is currently operational
The second objective was to applied the developed model to the case of a large-scale gallery. At the present time, we have reached the final stage of these simulations, by performing a sensitivity study to highlight the effect of permeability variations, the effect of variations of H2 entry pressure or the influence of the type of gas relative permeability formulation
The last part of this task is to present and publish the results to the scientific community. The writing of an article is under process while the presentation of the results had to be postponed due to the crisis. This last point appears to be the only noticeable effect of the current situation on our work.

## Slide 8: About my research
Figure: Supercontainer reference design,
adapted from [2].
Host rock
Main gallery
Storage alveole
Figure: Conceptual scheme of a deep geological disposal,
adapted from [1].
Zone I:
gas transfers through the EDZ
Zone II:
gas transfers in the sound rock layers
Controlled by the hydraulic properties modifications induced by fracturation
Governed by the rock structure at a micro-level
4
Notes: Within task 2, we planned to focus especially on the subtask 2.2, dedicated to advection, with the aim of conceptualizing the gas transport mechanisms at micro and macro scales.
To that end, we are interested:
- on the one hand in gas transfers through the excavation damaged zone
on the other hand in gas migrations in the sound rock layers
For those who wants to now exactely where Liège, where we did the first annual meeting

## Slide 9: About my research
Development of a multi-scale model in the FE2 method [6]
Step 1: Hydraulic microscopic model
Formulation, implementation and validation of the constitutive laws at the microscale (REV) without influence of mechanics.
Step 2: Hydro-mechanical microscopic model
Formulation and implementation of the constitutive laws at the microscale (REV) considering
  influence of mechanics.
  Hydro-mechanical couplings
In the sound rock layers:
c
>
Macroscopic scale
Microscopic scale
5
Notes: So far, our work focussed on the modelling of gas transfers in the EDZ.
The first objective was to develop a numerical model capable of reproducing the argillaceous rock environment surrounding the deep geological disposal. It can first be considered as a multiphysics porous medium. Moreover to properly model the localisation processes characterizing this zone, we have rather recourse to a model of second gradient type. And finally, a permeability evolution with strain has also been integrated into the model.
This model is currently operational
The second objective was to applied the developed model to the case of a large-scale gallery. At the present time, we have reached the final stage of these simulations, by performing a sensitivity study to highlight the effect of permeability variations, the effect of variations of H2 entry pressure or the influence of the type of gas relative permeability formulation
The last part of this task is to present and publish the results to the scientific community. The writing of an article is under process while the presentation of the results had to be postponed due to the crisis. This last point appears to be the only noticeable effect of the current situation on our work.

## Slide 10: About my research
Development of a multi-scale model in the FE2 method [6]
Step 1: Hydraulic microscopic model
Formulation, implementation and validation of the constitutive laws at the microscale (REV) without influence of mechanics.
Step 2: Hydro-mechanical microscopic model
Formulation and implementation of the constitutive laws at the microscale (REV) considering
  influence of mechanics.
  Hydro-mechanical couplings
Step 3: Hydro-mechanical macroscopic model
Implementation of the model in the FE2 framework
Experimental validation of the coupled hydro-mechanical model
Variability study at the scale of the sample
In the sound rock layers:
FE calculations
REV
FE calculations
Homogeneisation
>
Microscopic scale
Macroscopic scale
5
Notes: So far, our work focussed on the modelling of gas transfers in the EDZ.
The first objective was to develop a numerical model capable of reproducing the argillaceous rock environment surrounding the deep geological disposal. It can first be considered as a multiphysics porous medium. Moreover to properly model the localisation processes characterizing this zone, we have rather recourse to a model of second gradient type. And finally, a permeability evolution with strain has also been integrated into the model.
This model is currently operational
The second objective was to applied the developed model to the case of a large-scale gallery. At the present time, we have reached the final stage of these simulations, by performing a sensitivity study to highlight the effect of permeability variations, the effect of variations of H2 entry pressure or the influence of the type of gas relative permeability formulation
The last part of this task is to present and publish the results to the scientific community. The writing of an article is under process while the presentation of the results had to be postponed due to the crisis. This last point appears to be the only noticeable effect of the current situation on our work.

## Slide 11: References
Ensi (2013) Geologische Tiefenlager, Radioaktive abfälle sicher entsorgen, Rapport, 2013.
M. Van Geet, R. Gens (Ondraf/Niras 2014), Research on the long-term evolution of high-level waste forms in the frame of the Belgian research programme on geological disposal of high active and/ or long lived waste 19th Exchange Meeting– Rev. IFP, Vol. 60, No. 1, pp. 121-139.
F. Collin, Couplages thermo-hydro-mecaniques dans les sols et les roches tendres partiellement saturés, Doctoral thesis, University of Liege, 2003.
B. Pardoen, S. Levasseur, and F. Collin, Using Local Second Gradient Model and Shear Strain Localisation to Model the Excavation Damaged Zone in Unsaturated Claystone. Rock Mech. Rock Eng., 48(2):691-714, 2015.
B. Pardoen, S. Levasseur, and F. Collin, Excavation damaged zone modelling including hydraulic permeability evolution in unsaturated argilaceous rock, In:Khalili N, Russell AR, Khoshghalb A, eds. Unsaturated soils:research and applications. London: CRC Press, 387–1393, 2014.
B. Van Den Eijnden, P. Bésuelle, F. Collin & R. Chambon, Doublescale modelling of hydromechanical coupling and anisotropy in localization problems, International Symposium on Geomechanics from Micro to Macro, vol. 2, pp. 857-862, 2014.
6
Notes: References