## Slide 1
Damien ERNST, Xavier FETTWEIS, Michaël FONDER and Julie LOUIS
Extreme engineering for fighting climate change and the Katabata project

## Slide 2
80% of our primary energy comes from fossil fuels.
This percentage has hardly changed in the past decade.
CO2 concentrations are climbing at a record pace.
And now ? Extreme engineering solutions are needed.

## Slide 3: Global grid: The extreme electrical network
Fact 1: Natural smoothing of renewable energy sources and loads variability in a global grid setting. Very little investment in storage needed.
Fact 2: Renewable electricity – in €/MWh – is very cheap in high-density renewable energy fields (e.g., Atacama desert for solar energy, Greenland coast for wind energy).
Fact 3: Transporting electricity over long-distances is becoming cheap.
Fact 1 + Fact 2 + Fact 3 offer a true possibility for putting fossil fuels out of business for electricity generation (even without a CO2 tax) by building a global grid.

## Slide 4
Schematic representation of the backbone electricty interconnection.

## Slide 5: Why should Europe harvest wind energy in Southeastern Greenland?
High wind speeds.
Decorrelation with European wind temporal variability.
Huge areas. No NIMBY issues.
Half-way between Europe and the US.
Nice flagship project for accelerating the building of the global grid.

## Slide 6
Winds in Southeastern Greenland
In the southeastern part of Greenland, general circulation (synoptic) winds (driven by the Sun’s energy) add up to Katabatic winds.
Katabatic winds are the result of heat transfer processes between the cold ice cap and the warmer air mass above it.
When the air mass temperature is higher than that of the ice sheet, the former is cooled down by radiation, thus the air density increases forcing it down the sloping terrain.
The flow of katabatic winds is driven by gravity, temperature gradient and inclination of the slope of the ice sheet.

## Slide 7
Winds in Southeastern Greenland
Pure katabatic wind
Real katabatic wind
(deviated on its right due to the Coriolis force)
Synoptic wind due to the inland low pressure.
In this area, combination of both katabatic and synoptic winds

## Slide 8
We relied on data reanalysis and simulations to reconstruct wind signals from past in-situ and satellite observations.
The regional MAR (Modèle Atmosphérique Regional) model was used to simulate the weather over Greenland. This model can accurately represent physical processes in polar regions, including Katabatic winds, and has high spatial and temporal resolutions. Boundary conditions determined by the ERA5 reanalysis model.
Hourly values of wind speed at 100 meters above ground level are generated using the reanalysis models for the period 2008-2017.
Data acquisition for our analysis

## Slide 9: Regions selection for our analysis
Two areas in Greenland: one offshore (GROFF) and one onshore (GRON).
Temperatures too mild to have a frozen sea or permanent ice on-shore.
Two areas in Europe: one offshore wind farm in Denmark (DK) and one on-shore wind farm in France (FR).

## Slide 10
  Wind ressource assessment
Higher mean wind speeds in Greenland than in the two European locations.
Distribution of wind speeds more asymmetric for GRoff and GRon than for DK and FR.
The high standard deviations of the wind speeds in Greenland do not correspond to a high turbulence intensity, but to the strong influence of seasonality of the local natural resource.

## Slide 11: Load factors of the wind farms
Single turbine and wind farm transfer functions. Example of wind farm power curve aggregation based on multiple aerodyn SCD 8.0/168 units.
Capacity factors for the different locations

## Slide 12
Highest wind speed observed
Capacity factors versus
cut-out wind speed for the wind turbines.
Important remarks for manufacturers of wind turbines willing to tap into the Greenland wind energy market:
Wind turbines capable of operating with higher cut-out speed lead to significantly higher capacity factors in Greenland.
May also be interesting to design wind turbines which saturate in terms of power output for higher wind speeds (i.e., turbines having a higher rated output speed).

## Slide 13
Katabata project
Goal of the project: installing three weather stations in the South-East of Greenland.
The wind in this area has never been properly measured before!
The team:
Dr. Xavier Fettweis, Michaël Fonder
and Prof. Damien Ernst

## Slide 14
Location of the weather stations
AWS1 (synoptic wind + see breezes)
AWS2 (both winds)
+ venturi effect
AWS3 (local katabatic winds)
Zoom on AWS3

## Slide 15
Winds at those locations
Weather stations

## Slide 16
Vaisala’s AWS310 stations
Description of AWS310 stations:
4 sensors:
  Anemometer for wind speed
  Weathervane for wind direction
  Thermometer
  Humidity sensor
Satellite antenna for data transfer
10m mast with three guy wires
Battery with photovoltaic panel for lengthy operations in complete autonomy
Our AWS310s are also synonyms for an epic delivery:
Packages weighing more than 350kg for a total volume of 2m³ divided in seven boxes for each station
A total delivery delay of three months

## Slide 17
Departure from Saint-Malo

## Slide 18
10 bunks
Sufficient food for 3 months
15m length, 18m mast
Reinforced aluminium hull
Extra-large fuel tanks
Photos © Studio Corsaire
Northabout : a boat designed for polar expeditions

## Slide 19: Final preparations in Roscoff

## Slide 20
Crossing the Atlantic

## Slide 21
Crossing the Atlantic
(artist representation)

## Slide 22
Snapshots of life onboard

## Slide 23
Arrival in Greenland

## Slide 24
Icebergs are everywhere!
Lack of concentration could lead to catastrophic damage.
Sailing challenges in Greenland

## Slide 25
Station 1
Station 3
Station 2
Narsaq
Aappilattoq
Nanortalik
Delivery and blank test of the stations in Narsaq
Use of Nanortalik as operational base for Stations 1 and 2
Use of Aappilattoq as operational base for Station 3 and maintenance
Our stops in South Greenland

## Slide 26
Narsaq :
Incoming boxes

## Slide 27
Installing a station is a challenging task:
Planning all details on the boat
Transferring everything ashore
Finding the right spot for the station
Getting everything on site
Starting the installation, hoping for the best
Dealing with unpredictable weather
Photos © Julien Fumard
Installing a station is easier said than done!

## Slide 28
Transporting a station ashore

## Slide 29
Finalizing the installation of Station 1

## Slide 30
Aappilattoq, our last sheltered stop

## Slide 31
All stations encountered some critical issues a few days after their installation
Need for going back to the installations sites for repairs! Done by hiring a local fisherman.
Unforseen need for early maintenance

## Slide 32
All 3 stations are now operational
and sending data

## Slide 33
First comparison: MAR vs observations
MAR is able to simulate both spatial and temporal variability observed until now at the 3 stations
AWS1
AWS2
AWS3
Correlation: 0.87
Bias=+2.4km/h RMSE=11km/h
Mean: 34±20km/h
Correlation: 0.9
bias=-2km/h
RMSE=10km/h
Mean: 29±23km/h
1 observation every 20m
from 6 SEP 2020 to 15 OCT 2020
Correlation: 0.86
bias=+4km/h
RMSE=11km/h
Mean: 17±17km/h
Problem with the censor when high wind speeds
Wind measured at 10m

## Slide 34
Katabata 2?
First observations confirm the MAR results over the South of Greenland and the high wind speed in this area. Weather stations could be installed in other locations.
Next step (summer?):
Moving the weather stations to these area

## Slide 35: Direct air CO2 capture
Process commercialized by Carbon Engineering for capturing CO2. Air exits with a CO2 concentration of around 110 ppm. Energy required per ton of CO2 captured and compressed at 150 bars: around 1.4 MWh of heat (at a temperature of more than 600 °C for the calciner – provided now by burning natural gas) and 0.4 MWh of electricity.
Source: htts://carbonengineering.com/

## Slide 36: What can be done with this CO2?
Storing CO2 underground.
2. Synthesize synthetic green fuels with high energy density using hydrogen produced from water electrolysis and renewable electricity.
Example: the Sabatier reaction for producing CH4
3. Transform CO2 into graphite (pure coal) using, for example, the Bosch reaction, and building a mountain of coal.
High-temperature heat input can help optimise Solutions 2. and 3.

## Slide 39
Energy needed to return to 280 ppm
There are around 3.25 x 1012 tons of CO2 in the atmosphere. To return to preindustrial levels (280 ppm), (412−280)/412 * 3.25 x 1012=1.04 x 10exp(12) tons of CO2 have to be removed from the atmosphere.
Removing 1 ton of CO2 from the atmosphere requires (1.4+0.4)=1.8 MWh.
One ton of graphite generates 8.9 MWh when combusted. Due to the energy conservation principle, transforming one ton of CO2 into graphite and O2 would at least require 12/((2∗16+12)) * 8.9 = 2.42 MWh of energy.
Transforming 1.05 x 1012 of CO2 into graphite would require a minimum of 4,431,000 TWh of energy. This is 40 times our annual final energy consumption.

## Slide 40: Wouldn’t it be nice to be able to import 125 TWh of cheap synthetic green CH4 in Belgium?

## Slide 41
Remote renewable energy hub

## Slide 42
Artist representation of an infrastructure where solar energy and direct capture of CO2 in the air are used to produce green CH4. The green gas is then liquefied and shipped to consumption centers.

## Slide 43
Artist representation of a remote energy hub placed in Greenland.

## Slide 44
Remote renewable energy hub in Greenland: cost breakdown
Methane comes at a price 76.4 €/MWh in Zeebrugge.

## Slide 45: References
Berger, M., Radu, D., Fonteneau, R., Henry, R., Glavic, M., Fettweis, X., Le Du, M., Panciatici, P., Balea, L. & Ernst, D. (2018). Critical Time Windows for Renewable Resource Complementarity Assessment. Available at https://arxiv.org/abs/1812.02809
Radu, D., Berger, M., Fonteneau, R., Hardy, S., Fettweis, X., Le Du, M., Panciatici, P. Balea, L. & Ernst, D. (2019). Complementarity Assessment of South Greenland Katabatic Flows and West Europe Wind Regimes. Energy. Available at http://hdl.handle.net/2268/230016
Berger, M., Radu, D., Fonteneau, R., Deschuyteneer, T. & Ernst, D. (2020). The Role of Power-to-Gas and Carbon Capture Technologies in Cross-Sector Decarbonisation Strategies. Electric Power Systems Research. Available at http://hdl.handle.net/2268/235110
Study Committee: C1 WG: C1.35 (2020). Global electricity network – Feasibility. CIGRE Technical Report 775. Available at http://hdl.handle.net/2268/239969