## Slide 1
STEEL SHEET PILES EXPOSED TO FIRE
EXPERIMENTAL TESTS AND NUMERICAL MODELLING
Jean-Marc Franssen, João Martins
Liege University - ArcelorMittal
11th SiF conference
3°/11-02/12/2020

## Slide 2
Underground car park with concrete piles

## Slide 3
Underground car park with steel sheet piles

## Slide 4
STEEL sheet pile  Fire !!!
Can we protect ?
Yes
Anyway, we have to prove the fire resistance

## Slide 5
1) Thermal calculation of the temperatures in the steel sheet piles.
Thermal properties of steel: OK
Thermal properties of concrete or thermal insulation: OK
Physical phenomena in the ground : complicated (water movements)
Equivalent thermal properties of soils ? => Tests.
=> Simple approach is required: conduction with « evaporation » of moisture taken into account (movements not modelled explicitly)

## Slide 6
Furnace

## Slide 7
Installation of a thermocouple tree

## Slide 8
4 tests made:
Sand: saturated with water
not saturated
Clay: saturated with water
not saturated
Sheet piles – furnace
after one test

## Slide 9
Thermal conductivity
Specific heat

## Slide 11
Temperatures computed by SAFIR®

## Slide 12
2) Loading from the ground
Traditional approach: linearly z dependent functions
OK in static equilibrium

## Slide 13
During the fire, the structure is subjected to large horizontal displacements
away from the ground
to the ground

## Slide 14
New SPRING finite element
Characterised by
One single node
One direction
One relationship (Force – displacement)

## Slide 15
3) Complex construction phases
Installation of the sheet piles
Lower the water table
Excavation (partial)
Temporary supports (struts)

## Slide 16
Installation of the sheet piles
Lower the water table
Excavation (partial)
Temporary supports (struts)

## Slide 17
Installation of the sheet piles
Lower the water table
Excavation (partial)
Temporary supports (struts)
Utilisation of anchors (temporary or permanent)
Casting the slabs
Water table to original position

## Slide 18
The situation in our system when the fire starts results from all these phases:
in terms of displacements
in terms of pressure from the ground
Need of a specialised software:
RIDO
Model the complex sequence of construction phases
Produces the situation in the system after completion
=>
Input file
=>
SAFIR

## Slide 19
2 application examples:
A steel sheet pile
A concrete tunnel

## Slide 20
FIRE
Pressure from the ground: cold condition

## Slide 21
Pressure from the ground: fire condition

## Slide 22
Bending moments: cold condition

## Slide 23
Bending moments: fire condition

## Slide 24
13 tunnels in Poland
Length: from 300 m to 3 860 m
Diameter: 10 meters
Courtesy: Egis Rail / Egis Tunnel France

## Slide 25
½ loading
Variation of pressure compared to a static loading
Bending moment diagram

## Slide 26
Full loading
Variation of pressure compared to a static loading
Bending moment diagram

## Slide 27
60 minutes fire
Variation of pressure compared to a static loading
Bending moment diagram

## Slide 28
120 minutes fire
Variation of pressure compared to a static loading
Bending moment diagram

## Slide 30
Thank you