## Slide 1
1 University of Liège
A multiscale model to investigate gas migrations in clay materials
Gilles Corman1, Frédéric Collin1
Third International Workshop on the Finite Element Code LAGAMINE
5-7 July 2022 • Grenoble/ Villard-de-Lans (France)

## Slide 2
Context
01/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022
441 operational reactors
10% of the global electric capacity (392 GW)
54 reactors under construction
Production of long-lasting and high-level radioactive wastes, harmful to the biosphere
Deep geological disposal
Global civil nuclear energy in a nutshell, modified after Kernenergie (2021).

## Slide 3
Context
02/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022
Conceptual scheme of a deep geological disposal, adapted from ENSI (2013).
Multi-barriers confinement concept

## Slide 4
Context
02/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022
Conceptual scheme of a deep geological disposal, adapted from ENSI (2013).
Multi-barriers confinement concept
Supercontainer reference design, adapted from Grunwald (2021).

## Slide 5
Context
02/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022
Conceptual scheme of a deep geological disposal, adapted from ENSI (2013).
Multi-physical (THMC) processes
Multi-barriers confinement concept
Supercontainer reference design, adapted from Grunwald (2021).

## Slide 6
Context
02/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022
Multi-physical (THMC) processes
Multi-barriers confinement concept
Conceptual scheme of a deep geological disposal, adapted from ENSI (2013).
Corrosion
Gas release
Gas pressure build-up
Potential gas migrations through the barrier
Supercontainer reference design, adapted from Grunwald (2021).

## Slide 7
Context
02/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022
Conceptual scheme of a deep geological disposal, adapted from ENSI (2013).
Supercontainer reference design, adapted from Grunwald (2021).
Gas migrations in the sound rock layers
Governed by the rock structure at a micro-level
Development of a Multi-Scale Model
  Complexity and heterogeneity of the microstructure
  (pore network morphology, bedding planes)
  Hydro-mechanical effects
  Boom Clay easily transposed to other host rock formations
Governed by the hydraulic properties modifications induced by fracturation
Gas migrations in the EDZ
Corman et al. (2022) under review

## Slide 8
Table of content
03/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022
Context
Description of the model
Characterisation of parameters
Applications
Conclusion

## Slide 9: Purpose
Description of the model
Initial fracture in sample
Sr [-]
0.998
0.645
Cox Sample
Sr [-]
0.998
0.966
Macroscale models
No representation of local phenomena
Gerard et al. (2014)
Embedded fracture model, from Gerard et al (2014).
04/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022

## Slide 10: Purpose
Description of the model
Initial fracture in sample
Sr [-]
0.998
0.645
Macroscale models
No representation of local phenomena
Enriched with embedded fracture model to discern localised pathways
Gerard et al. (2014)
Olivella et al. (2008)
Nanoscale models
Time-consuming computation
Refined modelling at very low scale of all the pore structure complexity (size, tortuosity, network connectivity,…)
Yu et al. (2019)
Intermediate-level multiscale models
Based on experimental evidences that some defects within bedding planes and pre-existing fractures govern gas flows
Realistic microstructure including basic ingredients, to reproduce macro-properties (porosity, retention curve, permeability)
Gonzalez-Blanco (2017)
Embedded fracture model, from Gerard et al (2014).
From pore network to molecular model, from Yu et al. (2019).
04/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022

## Slide 11: Idealisation of the microstructure (REV)
Description of the model
1 fracture = bedding plane
w
w
w
w
A pore network
Conceptual scheme of the REV geometry
Half-interdistance between two bedding planes
Internal microstructure of Boom Clay sample using filled-emission scanning electron microscopy (FESEM), from Gonzalez-Blanco (2017)
05/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022
Bertrand (2020)

## Slide 12: Idealisation of the microstructure (REV)
Description of the model
1 fracture = bedding plane
w
w
w
w
A pore network substituted by an assembly of tubes
Half-interdistance between two bedding planes
Conceptual scheme of the REV geometry
Internal microstructure of Boom Clay sample using filled-emission scanning electron microscopy (FESEM), from Gonzalez-Blanco (2017)
05/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022
Bertrand (2020)

## Slide 13: Idealisation of the microstructure (REV)
Description of the model
1 fracture = bedding plane
w
w
w
w
A pore network substituted by an assembly of tubes
Bridging planes
Half-interdistance between two bedding planes
Internal microstructure of Boom Clay sample using filled-emission scanning electron microscopy (FESEM), from Gonzalez-Blanco (2017)
Conceptual scheme of the REV geometry
05/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022
Bertrand (2020)

## Slide 14: Behaviour of the REV components
Description of the model
Intrinsic permeability (Navier-Stokes)
Fracture – Bridging plane
Tube
Relative permeability curves (multi-phase flow) Yuster et al. (1951)
Retention curve Van Genuchten (1980) (Laplace equation)
Mechanical aperture Goodman (1976)
Evolution of the entry pressure
with the tube diameter:
06/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022

## Slide 15
Table of content
03/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022
Context
Description of the model
Characterisation of parameters
Applications
Conclusion

## Slide 16
Characterisation of the microstructural parameters
FESEM | -CT
150 – 270 | 410 – 560
FESEM | 
Experimental estimations of bedding plane separation, from Gonzalez-Blanco (2017)
Bedding
Tubes
1. Size of the REV
Bedding plane separation
2. Macroporosity
Fitting of the pore size distribution
Effect of small-size pores
(Tortuosity = Calibration factor)
07/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022

## Slide 17
Characterisation of the microstructural parameters
FESEM | -CT
150 – 270 | 410 – 560
FESEM | 
Bedding
Tubes
1. Size of the REV
Bedding plane separation
07/17
2. Macroporosity
Fitting of the pore size distribution
Effect of small-size pores
(Tortuosity = Calibration factor)
Experimental estimations of bedding plane separation, from Gonzalez-Blanco (2017)
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022

## Slide 18
Characterisation of the microstructural parameters
FESEM | -CT
150 – 270 | 410 – 560
FESEM | 
Bedding
Tubes
1. Size of the REV
Bedding plane separation
Fracture aperture
Macropores
3. Intrinsic permeability
Effect of large-size pores
07/17
2. Macroporosity
Fitting of the pore size distribution
Effect of small-size pores
(Tortuosity = Calibration factor)
Experimental estimations of bedding plane separation, from Gonzalez-Blanco (2017)
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022

## Slide 19
Characterisation of the microstructural parameters
6. Normal stiffness of the fracture
Goodman (1976)
5. Retention curve
Van Genuchten (1980)
4. Relative permeability curves
Yuster et al. (1951)
08/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022

## Slide 20
Table of content
03/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022
Context
Description of the model
Characterisation of parameters
Applications
Conclusion

## Slide 21: One-element simulation
Applications
Bedding plane separation:
Bedding plane aperture:
0.1
Tubes diameter
Bridging plane aperture
Injection test
Mechanically blocked
Water pressure increase
  3MPa to 5MPa
Gas pressure imposed at 3MPa
2m
Loading
Response
5
3
09/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022

## Slide 22: One-element simulation
Applications
Bedding plane separation:
Bedding plane aperture:
0.1
Tubes diameter
Bridging plane aperture
Injection test
Mechanically blocked
Water pressure increase
  from 3MPa to 5MPa
Gas pressure imposed at 3MPa
2m
Bedding
Loading
Bedding + n tubes
Localisation
Loading
Bedding + n tubes
+ Bridging planes
Homogenisation
Response
Response
5
3
09/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022

## Slide 23: One-element simulation
Applications
Porosity distribution for the tubes
1 fracture
Water flux
10-6
10-7
10-8
10-9
10-10
10-11
0 1 2 3 4 5
Time [days]
10/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022

## Slide 24: One-element simulation
Applications
Fracture-controlled flow
Porosity distribution for the tubes
Water flux
10-6
10-7
10-8
10-9
10-10
10-11
0 1 2 3 4 5
Time [days]
10/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022
1 fracture + (micro) tubes

## Slide 25: One-element simulation
Applications
Porosity distribution for the tubes
Effect of large pores
Fracture-controlled flow
Water flux
10-6
10-7
10-8
10-9
10-10
10-11
0 1 2 3 4 5
Time [days]
10/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022
1 fracture + all tubes

## Slide 26: Gas injection experiment
Applications
Gonzalez-Blanco (2017)
Geometry and boundary conditions
Parameters
Reservoirs
Stiff elements:
Highly conductive:
Flat retention curve:
Boom Clay matrix
Mechanical:
Hydraulic:
  Initial aperture:
  Initial permeability:
  Initial porosity:
  Pore distribution: 15 tubes with
Boom Clay Zone of Fracture Development (ZFD)
Initial aperture: increased by 1 order of magnitude
Fracture stiffness: decreased by 2 orders of magnitude
11/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022
Upstream reservoir
Boom Clay Sample
Downstream reservoir
0.017m
0.020m
0.034m
0.025m
0.001m
ZFD

## Slide 27: Gas injection experiment
Applications
Gonzalez-Blanco (2017)
12/17
Stage 1
Stage 2
Stage 3
Simulation stages
0-500 [min]
500-745 [min]
745-1080 [min]
1080-2300 [min]
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022

## Slide 28: Gas injection experiment
Applications
Gonzalez-Blanco (2017)
13/17
Time [s]
4800
17800
30000
32000
Gas pressure [Pa]
Height [m]
0.06
0.05
0.04
0.03
0.02
0.01
0
0
2
4
6
8
105
0.07
0
Step 1 – Effect of microstructure components
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022

## Slide 29: Gas injection experiment
Applications
Gonzalez-Blanco (2017)
13/17
Step 1 – Effect of microstructure components
Time [s]
4800
17800
30000
32000
Gas pressure [Pa]
Height [m]
0.06
0.05
0.04
0.03
0.02
0.01
0
0
2
4
6
8
105
0.07
0
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022

## Slide 30: Gas injection experiment
Applications
Gonzalez-Blanco (2017)
13/17
Step 1 – Effect of microstructure components
Time [s]
4800
17800
30000
32000
Gas pressure [Pa]
Height [m]
0.06
0.05
0.04
0.03
0.02
0.01
0
0
2
4
6
8
105
0.07
0
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022

## Slide 31: Gas injection experiment
Applications
Gonzalez-Blanco (2017)
14/17
Steps 1&2&3 – Fractures properties
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022

## Slide 32: Gas injection experiment
Applications
Gonzalez-Blanco (2017)
15/17
Steps 2&3 – Pressures evolution
Start air dissip.
End air dissip.
Exp.
Num.
Num. frac.
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022

## Slide 33: Gas injection experiment
Applications
Gonzalez-Blanco (2017)
15/17
Steps 2&3 – Pressures evolution
Start air dissip.
End air dissip.
Exp.
Num.
Num. frac.
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022

## Slide 34: Gas injection experiment
Applications
Gonzalez-Blanco (2017)
15/17
Steps 2&3 – Pressures evolution
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022
Evolution of the entry pressure
with the tube diameter:
Exp.
Num.
Num. frac.

## Slide 35: Gas injection experiment
Applications
Gonzalez-Blanco (2017)
16/17
Steps 2&3 – Maps of gas pressure
0 [min]
245 [min]
End phase 2
500 [min]
800 [min]
1800 [min]
End phase 3
1e4
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022

## Slide 36
Table of content
03/17
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022
Context
Description of the model
Characterisation of parameters
Applications
Conclusion

## Slide 37
Conclusions
17/17
We developed a multi-scale model able to
  Simply idealise the microstructure of the rock with fractures and tubes
  Reproduce mechanisms inherent to gas migrations in sound rock layers
We showed that
  Macropores, micropores and fractures play different roles in gas flows
  Preferential flow paths can be generated through fractures with weaker properties
We plan to
  Release the mechanics at the macroscopic scale
  Derive and validate a general formulation linking air entry pressure to fracture aperture
  Extent the developments to gas flows perpendicular to bedding planes, using bridging planes
  Integrate uncertainty by performing random drawing on the weaker bedding planes
  Keep the model general enough to cope with other kinds of host rocks
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022

## Slide 38: Thank you for your attention
Third International Workshop on the Finite Element Code LAGAMINE
5-7 July 2022 • Grenoble/ Villard-de-Lans (France)

## Slide 39
Kernenergie (2021), L’énergie nucléaire dans le monde, Retrieved April 8, 2021 from https://www.kernenergie.ch/.
N. Grunwald. et al. (2021): Non-isothermal two-phase flow in deformable porous media: Systematic open-source implementation and verification procedure, Geomechanics and Geophysics for Geo-energy and Geo-Resources (submitted)
P. Gerard et al (2014), Modelling of localised gas preferential pathways in claystone, International Journal of Rock Mechanics and Mining Sciences, 67:104-114.
S. Olivella, EE. Alonso (2008), Gas flow through clay barriers. Géotechnique, 58:157-68.
L. Gonzalez-Blanco (2017), Gas migration in Deep Argillaceous Formations: Boom Clay and Indurated Clays, Doctoral thesis, Universitat Politècnica de Catalunya.
H. Yu, Y. Zhu, X. Jin, H. Liu, H. Wu (2019), Multiscale simulations of shale gas transport in micro/nano-porous shale matrix considering pore structure influence, Journal of Natural Gas Science and Engineering, Volume 64, Pages 28-40.
F. Bertrand (2019), Hydro-mechanical modelling of multiphase flow in naturally fractured coalbeds applied to CBM recovery or CO2 storage, Doctoral thesis, University of Liège.
P. Bésuelle, G. Viggiani, JJM. Desrues, C. Pascal (2014), A Laboratory Experimental Study of the Hydromechanical Behavior of Boom Clay, Rock Mechanics and Rock Engineering.
G. Volckaert, L. Ortiz, P. De Canniere, M. Put, S.T. Horseman, J.F. Harrington, V. Fioravante, M. Impey (1995), MEGAS Modelling and experiments on gas migration in repository host rocks. EUR 16235 MEGAS Final Report Phase 1, p.464.
S. Yuster et al. (1951), Theoretical considerations of multiphase flow in idealized capillary systems, In Proceedings of the 3rd World Petroleum Congress, Section II, The Hague, Volume 2, Pages 437-445.
R.E. Goodman (1976), Methods of geological engineering in discontinuous rocks.
M. T. Van Genuchten (1980), A closed-form equation for predicting the hydraulic conductivity of unsaturated soils. Soil science society of America journal, 44(5):892–898.
References
3rd International Workshop on the Finite Element Code LAGAMINE – July 2022

## Slide 40: Computation of the model
Definition of the REV
Definition of the REV component behaviours
General principles for the computation of the model
3.1 Hydraulic network respecting these conditions:
  Anti-symmetric boundary fluxes
  Macroscopic pressure gradient between the boundaries
6
B
1
2
5
3
4
7
1
3
2
6
L
R
T
4
5

## Slide 41: Computation of the model
Definition of the REV
Definition of the REV component behaviours
General principles for the computation of the model
3.1 Hydraulic network respecting these conditions:
  Anti-symmetric boundary fluxes
  Macroscopic pressure gradient between the boundaries
3.2 Hydraulic problem established through mass balance on each node (j)
with where Flow model for the channel i
j
i
i-1
i+1

## Slide 42: Computation of the model
Definition of the REV
Definition of the REV component behaviours
General principles for the computation of the model
3.1 Hydraulic network respecting these conditions:
  Anti-symmetric boundary fluxes
  Macroscopic pressure gradient between the boundaries
3.2 Hydraulic problem established through mass balance on each node (j)
3.3 Hydraulic problem solved
  for a given mechanical configuration
  under steady-state conditions
  by applying the macro pressure to one node