## Slide 1
Application of deep learning for linking microscope image features to ionic signal distribution
Raphaël La Rocca1; Virginie Bertrand1; Eppe Gauthier1; Edwin De Pauw1; Loïc Quinton1
1Mass Spectrometry Laboratory, MolSys Research Unit, Department of Chemistry, University of Liège, Liège, Belgium
Contact: raphael.larocca@uliege.be
Microscope image
Mass spectrometry image
with a high spatial resolution
Input
Prediction
m/z
Goal
High spatial resolution of mass spectrometry imaging is difficult to obtain as it is time consuming and the reduction of ionized matter reduces the sensitivity.
Image fusion can increase artificially the spatial resolution of mass spectrometry images when combined with image modalities of a higher spatial resolution.
Fusion method with predictive capabilities are rare and also dependent on multiple image preprocessing.
Deep learning methods have shown to be more robust for image analysis by avoiding any image preprocessing.
PC
[C46H84NO8P + H]⁺ 810.6016 m/z
PC
[C44H80NO8P + H]⁺ 782.5698 m/z
SM
[C41H77N2O6P + H]⁺ 725.5600 m/z
PE
[C29H50NO8P + H]⁺ 572.3343 m/z
PA
[C43H73O8P + H]⁺ 749.5124 m/z
PS
[C37H66NO9P + H]⁺
700.4548 m/z
CerP
[C38H68NO6P + H]⁺ 666.4858 m/z
HCCA
2HCCA H2Na+
U-net architecture is modified to fused microscopy and mass spectrometry images.
Estimate the lipid composition of cells by increasing the spatial resolution from 100 µm to 1.5 µm.
The cause of mass signal has to visible in the microscopic image.
Detect/annotate cell types directly from a microscope image with a trained model.
Fused image Segmentation
Microscope
image
MCF-7
WI-38
K-means segmentation with 3 clusters.
Clustering applied on monocultures.
Target classes: background, WI-38 cells and MCF-7 cells
Balanced accuracy:
Microscopic image: 0.56
Predicted fused image: 0.76
6) Predicted Fused Image
4) Fusion Method
3) Challenge
2) Goal
1) Motivation
WI-38
MCF-7
MCF-7 & WI-38
300 µm
300 µm
MODEL
m/z
Training on a mixed cell deposit of WI-38 and MCF-7 cells.
Testing on monocultures of WI-38 and MCF-7 cells separately.
MCF-7
WI-38
MODEL
MODEL
7) Unsupervised Cells segmentation
Microscope image
Segmentation
8) Conclusion
We thank the F.R.S. FRNS, EOS project Rhizoclip (grant number 30650620), the Interreg – Euregio MeuseRhin EurLipids project, and the EU_FT-ICR_MS H2020 project for financial support.
Acknowledgments
MCF-7
WI-38
5) Predicted signal comparison
Absolute correlation
Original mass signal
MSE
Signal
Signal
d) Mean square error between b) and c)
MCF-7
WI-38
PC(1)
PC(2)
SM
PE
PA
PS
HCCA
CerP
PE(1)
PC
SM
PE(2)
PA
PS
HCCA
CerP
Absolute correlation
Original signal
Predicted image
Predicted signal
Correlation of cell monoculture annotations with detected signal
The full microscope image is parsed in small images of 300 µm represented by 192x192 pixels with 3 color channels.
The mass spectrum associated to the parsed microscope image by registration is composed of 8 ions to simplify data interpretation.
a) Log of raw signal
b) Standardized signal
Signal
Predicted mass signal
c) Standardized signal
PC(1)
PC(2)
SM
PE
PA
PS
HCCA
CerP
PC(1)
PC(2)
SM
PE
PA
PS
HCCA
CerP
PC(1)
PC(2)
SM
PE
PA
PS
HCCA
CerP
PC(1)
PC(2)
SM
PE
PA
PS
HCCA
CerP
PC(1)
PC(2)
SM
PE
PA
PS
HCCA
CerP