## Slide 1
1 Geomechanics and Engineering Geology, University of Liège
Thermal effects on THM coupling behaviour of COx claystone in Excavation Damage Zone
Hangbiao Song1, Frédéric Collin1
6 July 2022 • Lagashop 2022, Grenoble (France)

## Slide 2
Context
02/16
Geological disposal of radioactive wastes
Multi-barrier confinement
Long-term management
THMC coupling process
Excavation, open drift, waste emplacement, backfilling, self-sealing, repository closure
Conceptual scheme of a deep geological disposal, modified from ENSI (2013)
Main gallery
Host rock
Storage alveole
Schematic view of repository concepts/disposal cells, modified from ANDRA (2005)
Callovo-Oxfordian claystone
Technological gap
Technological gap
Steel liner
(Carbon steel)
Disposal
package
(Carbon steel)
Waste canister
(stainless steel)
Scale
0 12.5 25cm

## Slide 3
Context
03/16
Near field:
Excess pore pressure
Fracture re-opening/propagation
Alter permeability
Pw
αw > αs
Thermal conduction
Rock layers
Thermal pressurization
Canister
T
Far field:
Tensile failure
Shear failure
Reactivate old fractures/faults
Natural
Temperature
Heated
Symmetric axes: No horizontal deformation
No horizontal heat/water flow, modified from Braun P., (2019)
Objective:
Reproduce the damage processes and the in-situ observations around EDZ induced by thermal effects.

## Slide 4
Table of content
04/16
Context
Description of the numerical model
Applications
Conclusions

## Slide 5: Shear strain localisation evidence
Representation of damage
From geomaterials failure…
Human-made slope failure (Belgium,1998)
Railway tracks after an earthquake (Turkey, 1999)
Biaxial compression test on sand, Desrues et al. (1999)
…to the drilling of underground galleries…
Mechanisms of rock mass failure around gallery, adapted from Diederichs (2003)
05/16
Boom Clay
COx claystone
…in host rock formations.
Fracturation pattern around storage galleries, Bastiaens et al. (2003) and Bernier et al. (2007)
75% of fractures in mode II (shear). Armand et al. (2014)

## Slide 6: Numerical considerations
Description of the numerical model
06/16
Imposed displacement
Impervious boundary
Constraint displacement
Material imperfection
Mesh size: variable
Deviatoric strain
increment
elements
elements
e1
e1 e2
e2
Deviatoric strain
increment
Classical FE methods:
Mesh size dependency
e1
Deviatoric strain increment
Regularisation technique:
Shear band width control
Collin et al. (2006)
e1e2
e2
Deviatoric strain
increment
e1
Regularisation technique Chambon et al. (1998)
Enrichment of the kinematics with microstructure effects
Macro-volume  Micro-volumes
Displacement
Deformation
Kinematics of microstructure continuum
Local 2nd gradient model:

## Slide 7: Balanced equations
Description of the numerical model
07/16
Water mass balance
Energy balance of mixture
Momentum balance of mixture
Field of Lagrange multipliers
Kinematic restriction
Microstructure effects
𝑓,𝑖 =

## Slide 8
Table of content
Context
Description of of the numerical model
Applications
Conclusions
04/16

## Slide 9: THM coupled processes - COx Claystone - Strain localisation during Heating ?
Applications
08/16
EURAD-HITEC Subtask 2.3 – THM modelling of effect of temperature in near field: selection of benchmark exercises
2D plane strain generic model
Lagamine: finite element code developed in ULiege
Gap=4.63 mm
Steel liner

## Slide 10: THM coupled processes - COx Claystone – Cross anisotropic Elastic response
Applications
09/16
Temperature
Convergence
Pore pressure
Elastic parameters | 
ρs (kg/m3) | 2639
n (-) | 0.18
E∥ (MPa) | 8000
E⊥ (MPa) | 5000
ν∥∥ (-) | 0.21
ν∥⊥ (-) | 0.35
G⊥ (MPa) | 2500
b∥ (-) | 0.83
b⊥ (-) | 0.87

## Slide 11: THM coupled processes - COx Claystone - Constitutive modelling
10/16
Applications
First gradient law: Van Eekelen criterion
Van Eekelen yield surface with hardening/softening
hyperbolic relation for two values of coefficient Bϕ
Van Eekelen (1980)
Second gradient law:
Mindlin, 1965
Internal length scale: control of bands’ width
Variation of cohesion for cross-anisotropic rock (fabric tensor):
(a) as a function of the angle between the normal to the bedding planes and the direction of loading and (b) as a function of the loading vector.
Niandou et al., (1997); Valès et al., (2004)

## Slide 12: THM coupled processes - COx Claystone – Strain localisation (THM)
11/16
Applications
Plasticity
Deviatoric strain increment
Total deviatoric strain
1e-3
1e-4
1e-5
T0+270 days
1e-3
1e-5
1e-5
T0+24 h
1e-3
1e-5
1e-5
T0+180 days
1e-3
1e-4
1e-5
T0+198 days
1e-3
1e-4
1e-5
T0+2 years
1e-3
1e-4
1e-5
T0+4 years
Plasticity
Deviatoric strain increment
Total deviatoric strain
Heating
Excavation
Waiting
1e-3
1e-5
1e-5
T0+8 years
1e-3
1e-5
1e-5
T0+10 years
3m×3m

## Slide 13: THM coupled processes - COx Claystone – stress path
12/16
Applications
Vertical axis
Horizontal axis
End of excavation
End of waiting

## Slide 14: THM coupled processes - COx Claystone – Increased gap
13/16
Applications
Gap=5.79mm
Plasticity
Deviatoric strain increment
Total deviatoric strain
(3m×3m)
1e-3
1e-7
1e-5
T0+237 days
Contact pressure
T0+180 days
T0+198 days
T0+237 days
T0+24 h
T0+180 days
T0+198 days
1e-3
1e-4
1e-5
T0+270 days
Gap=4.63mm
(3m×3m)
Plasticity
Deviatoric strain increment
Total deviatoric strain
Reference value

## Slide 15: THM coupled processes - COx Claystone – Increased gap
14/16
Applications
1e-7
1e-4
1e-3
T0+261 days
No support
Plasticity
Deviatoric strain increment
Total deviatoric strain
Comparison of convergence
Comparison of pore pressure
Vertical axis
Horizontal axis
Horizontal axis
Vertical axis
(5m×5m)
1e-3
1e-4
1e-3
T0+195 days
1e-4
1e-5
1e-3
T0+183 days

## Slide 16: THM coupled processes - COx Claystone – stress path (No liner)
15/16
Applications
End of excavation
End of waiting
Horizontal axis
Vertical axis

## Slide 17
Table of content
04/16
Context
Description of of the numerical model
Applications
Conclusions

## Slide 18
Conclusions
We developed a 2nd gradient THM coupled element able to
  Model damage around EDZ with strain localisation in shear band mode.
  Reproduce thermal effects on the in-situ THM behaviour of COx claystone.
We showed that
  During the heating, the shear strain localisation is highly pronounced.
  The gap plays a critical role in reproducing the in-situ coupling behaviour at EDZ, both the development of plasticity and shear bands.
16/16
We plan to
  A tensile failure criterion will be taken into account to better represent the extensional stress pathways.

## Slide 19: Thank you for your attention
1 Geomechanics and Engineering Geology, University of Liège
Hangbiao Song1, Frédéric Collin1
6 July 2022 • Lagashop 2022, Grenoble (France)

## Slide 20
Ensi (2013), Geologische Tiefenlager, Radioaktive abfälle sicher entsorgen Rapport.
Andra (2005), Dossier 2005: Argile Synthesis. Evaluation of the Feasibility of a Geological Repository in an argillaceous Formation Meuse/Haute-Marne Site. National Agency for Radioactive Waste Management, Paris.
P. Braun(2019), Thermo-hydro-mechanical behavior of the Callovo-Oxfordian. PhD thesis. Université Paris-Est.
J. Desrues and M. Mokni (1999), Strain localisation measurements in undrained plane-strain biaxial test on Hostun RF sand, Mech Cohes-Frict Mat, 4(4):419–441.
M. S. Diederichs (2003), Rock Fracture and Collapse Under Low Confinement Conditions, Rock Mech Rock Eng, 36(5):339–381.
W. Bastiaens, F. Bernier, M. Buyens, M. Demarche, X. L. Li, J.-M. Linotte, J. Verstricht (December 2003), The extension of the HADES underground research facility at Mol, Belgium, The construction of the connecting gallery, EURIDICE report 03-294.
F. Bernier, Y. Wileveau (2008), Similarities in the hydromechanical response of Callovo-Oxfordian clay and Boom Clay during gallery excavation, Physics and Chemistry of the Earth 33 S343–S349.
F. Collin, R. Chambon, and R. Charlier (2006), A finite element method for poro-mechanical modelling of geotechnical problems using local second gradient models, International Journal for Numerical Methods in Engineering, 65(11):1749-1772.
R. Chambon, D. Caillerie, and N. El Hassan (1998), One-dimensional localisation studied with a second grade model. European Journal of Mechanics, A/Solids, 17(4):637-656.
B. Pardoen (2015), Hydro-mechanical analysis of the fracturing induced by the excavation of nuclear waste repository galleries using shear banding, PhD Thesis, University of Liège, Faculty of Applied Sciences.
EURAD WP HITEC - Milestone report 49 – Selection of benchmark exercises for task 2.3.
Van Eekelen, H. A. M. (1980). Isotropic yield surfaces in three dimensions for use in soil me- chanics. Int J Numer Anal Meth Geomech, 4(1):98–101.
R. D. Mindlin (1965) , Second gradient of strain and surface-tension in linear elasticity. Int J Solids Struct, 1:417–438.
H. Niandou, J. F. Shao, J. P. Henry, and D. Fourmaintraux (1997), Laboratory investigation of the mechanical behaviour of tournemire shale. Int J Rock Mech Min Sci, 34(1):3–16.
F. Valès, D. N. Minh, H. Gharbi, and A. Rejeb (2004), Experimental study of the influence of the degree of saturation on physical and mechanical properties in tournemire shale (france). Appl Clay Sci, 26(1-4):197–207.
References

## Slide 21: THM coupled processes - COx Claystone – Elastoplastic results
10/16
Applications
Convergence
Pore pressure
Anisotropic parameters
Characteristics | Symbol | Value
Cohesion [MPa] |  | 4.1
 | A// | 0.117
 | b1 | 14.24
 | b2 | 0
Ratio of cohesion softening [-] | ξc | 5
Cohesion softening parameter [-] | Bc | 0.003
Cohesion softening shifting [-] | decc | 0
Initial compressive friction angle [°] | φc,0 | 10
Final compressive friction angle [°] | φc,f | 23
Initial extensive friction angle [°] | φe,0 | 7
Final extensive friction angle [°] | φe,f | 23
Friction angle hardening parameter [-] | Bφ | 0.001
Friction angle hardening shifting [-] | decφ | 0
Dilatancy angle [°] | ψc | 0.5
Second gradient elastic modulus [kN] | D | 15
Characteristics | Symbol | Value
Cohesion [MPa] |  | 4.1
 | A// | 0.117
 | b1 | 14.24
 | b2 | 0
Ratio of cohesion softening [-] | ξc | 5
Cohesion softening parameter [-] | Bc | 0.003
Cohesion softening shifting [-] | decc | 0
Initial compressive friction angle [°] | φc,0 | 10
Final compressive friction angle [°] | φc,f | 23
Initial extensive friction angle [°] | φe,0 | 7
Final extensive friction angle [°] | φe,f | 23
Friction angle hardening parameter [-] | Bφ | 0.001
Friction angle hardening shifting [-] | decφ | 0
Dilatancy angle [°] | ψc | 0.5
Second gradient elastic modulus [kN] | D | 15

## Slide 22: THM coupled processes - COx Claystone – Elastoplastic results
10/16
Applications
Fig. : Cohesion variation at: (a) Horizontal, (b) Vertical, (c) 45 degree directions.
(a)
(b)
(c)
Fig. : Stress path in vertical direction (r=1.25m)
Fig. : Cohesion in vertical direction

## Slide 23: Discussion
10/16
Applications
23
Since Mohr-Coloumb overestimates the tensile strength of rock material, the objective is to limit the plasticity caused by tensile stress, to implement the law with ranking tensile criterion.
σ’
’
Mohr-Coloumn
hyperbolic model
Ranking tensile criterion