## Slide 1: A comprehensive analysis of CO2 exchanges in agro-ecosystems based on a generic soil-crop model-derived methodology
Mathieu Delandmeter, Joël Léonard, Fabien Ferchaud, Bernard Heinesch, Tanguy Manise, Ariane Faurès, Jérôme Bindelle, Benjamin Dumont
Gembloux Agro-Bio Tech – University of Liege (Belgium)

## Slide 2: The idea
ICOS stations focus on specific pedo-climatic conditions and management

## Slide 3: The idea
ICOS stations focus on specific pedo-climatic conditions and management
Calibration and validation
Soil-crop model
Would enable the extrapolation to other contrasted pedo-climatic conditions and management
Climate change
Different crops
Tillage?

## Slide 4: The idea
ICOS stations focus on specific pedo-climatic conditions and management
Calibration and validation
Soil-crop model
Objectives
Elaborate, from field measurements, the methodology to compute CO2 fluxes.
Discuss the influence of various environmental drivers on crop rotations CO2 fluxes, based on both field observations and model simulations.

## Slide 5: The BE-LON experimental site
Experiment started in 2004
Data collected: yield, crop growth, soil variables…
But also CO2 and N2O exchanges
4-year crop rotation: sugarbeet, winter wheat and potatoes
https://www.icos-belgium.be/ESLonzee.php#Lonzee. Picture by Eli Verheyen in 2018

## Slide 6: The soil-crop model STICS
Plant development module
Nutrition module
Water balance module
Yield
Stresses
Soil bio-chemical state (SOC, N…)
Water balance
INPUTS
OUTPUTS
Model daily computation
Plant
Soil
Climate
Initialization
Management

## Slide 7: Methodology
Vegetative organs
Harvested organs
Belowground
(roots + rhizodeposition)
Ecosystem Respiration (RECO)
Autotrophic (maintenance + growth)
Heterotrophic
Gross Primary Productivity (GPP)
Fallen
leaves

## Slide 8: Methodology
Vegetative organs
Harvested organs
Belowground
(roots + rhizodeposition)
Ecosystem Respiration (RECO)
Autotrophic (maintenance + growth)
Heterotrophic
Gross Primary Productivity (GPP)
Fallen
leaves
Used a constant coefficient coming from shoot-root ratios and harvest indices, considering rhizodeposition (Bolinder et al., 2007).

## Slide 9: Methodology
Krinner et al. (2005)
Krinner et al. (2005)
Amthor (2000); Kirschbaum and Mueller (2001); Sun et al. (2007)
Brisson et al. (2009)
Delandmeter et al. (in preparation)
Bolinder et al. (2007)
Suleau et al. (2011)

## Slide 10: Results – Relationship between MR and plant N concentration
Following Amthor (2000), Kirschbaum and Mueller (2001) and Sun et al. (2007):
Delandmeter et al. (in preparation)

## Slide 11: Results – Carbon dynamics illustration
Delandmeter et al. (in preparation)
Winter wheat
2011-2012

## Slide 12: Results – Goodness of fit
Delandmeter et al. (in preparation)

## Slide 13: Results – Carbon budget
Delandmeter et al. (in preparation)

## Slide 14: NEE inter-annual variability
Potatoes
Sugarbeet
Maize
Cover crop
Correlations?
Qcum x NEE
NDAV x NEE
Temperature x NEE
(Precipitations – ETP) x NEE
Winter wheat
.
.
.
Delandmeter et al. (in preparation)

## Slide 15: NEE inter-annual variability
Objective: Quantify crop response to weather conditions
Increased period of active vegetation and/or radiation increases C sequestration, in agreement with e.g. Buysse et al. (2017) and Ceschia et al. (2010)
Delandmeter et al. (in preparation)

## Slide 16: NEE inter-annual variability
Delandmeter et al. (in preparation)
The crop model allows to differentiate respiration components.
Objective: Is HR more influenced by temperature than AR (Suleau et al., 2011)?
We found a greater influence of temperature on AR than HR, in agreement with e.g. Zhang et al. (2013).

## Slide 17: Conclusion
The approach computes daily CO2 fluxes (GPP, RECO, NEE) from soil-crop model outputs
The 16-year ICOS crop rotation of BE-LON was used to set-up the approach
Goodness of fit indicators proved the method to be reliable
Environmental drivers of CO2 fluxes inter-seasonal variability were identified
Its genericity makes it a valuable tool to investigate crop rotations CO2 dynamics
Picture by Eli Verheyen in 2018

## Slide 18: A comprehensive analysis of CO2 exchanges in agro-ecosystems based on a generic soil-crop model-derived methodology
Mathieu Delandmeter, Joël Léonard, Fabien Ferchaud, Bernard Heinesch, Tanguy Manise, Ariane Faurès, Jérôme Bindelle, Benjamin Dumont
Gembloux Agro-Bio Tech – University of Liege (Belgium)