## Slide 1
S. Calvo* , A. Delafosse et D. Toye
Department of Chemical Engineering – PEPs, University of Liege, Belgium
Use of numerical tools to improve solid-liquid reactor involved in pharmaceutical processes

## Slide 2: Difficulties in solid-liquid system involve in pharmaceutical processes
Scaling-up
Cell / algae / Microbial
culture
Difficulties
  Inhomogeneity
  Cristallization on walls
  Mass Transfert
  Constrains
    Shear stress
    Interface liquid-gas
    Over concentration du to additive addition
  Scaling up / Scaling-down
Vaccine formulation
Cristallization
Dissolution
Flocculation
Mechanical stresses

## Slide 3: 1. Ensuring product homogeneity from lab scale to industrial scale
Dose of vaccine
Inefficiency /
Dangerous
Homogeneous operating conditions at different scales
Production
Process scale-up
Lab Scale
?
Composition of attenuated vaccine with aluminum salts
AlPO4
Al(OH)3
Mélange à 50/50 d’
ρp = 2500 kg/m³
[C] = 0,74cm³/l
3

## Slide 4: 1. What is the main consideration for homogeneous suspension
Full Suspension
Homogeneous suspension
N ↗
N ↗
Njs prediction (Just supended speed)
Correlation of Zwietering
Full Suspension
Sedimentation
Tip speed
Volumic power input
Nhs prediction
N correlation
Analogy
extrapolation
extrapolation
Njs
Nhs
4

## Slide 5: 1. How to perform robust analysis with CFD for scaling-up
CFD Modelization
PIV Measure
Fluid flow validation
Suspension behaviour validation
Nhs
Measure
Caractérisation des particules
Rule for Scale-Up
5

## Slide 6: 1. Solid Particles characterization
Particles of aluminum salts
AlPO4
Al(OH)3
Mélange 50/50 Al
ρp = 2500 kg/m³
[C] = 0,74cm³/l
Laser granulometry
Sedimentation speed
Particule size evolution due to hydratation with no mixing
6

## Slide 7: 1. Simulation adaptation
Nhs Measure
CFD
Modelization
Nhs condition Simulation
Validation of suspension behaviour
+
Particle size validation
Numerical particle size adjustment
7

## Slide 8: 1. Exp. flow characterization by Particle Image Velocimetry (PIV)
Vitesse moyenne
Composante axiale
Particules:
Dp = 5-10µm
Dp = 20-50µm
16 x 16 pixels
Instantaneous velocities
Correlation
Mean local velocities
Instantaneous velocities
Velocity fluctuation
8

## Slide 9: 1. CFD Model
Particles
< 0,074%
µm < dp? < 100µm
Nhs = 20 RPM
« Eulerian Mixture »
« Eulerian Multiphase »
0,2 < Vol. Fraction < 16% + dp > 100µm
k-ε
Multiphase ≥ Mixture
continuity and momentum equation on a single phase mixture

continuity and momentum equation on both phase
Coupling of the different phases by the application of interfacial terms:
drag, added mass, lift force, slip velocity
« Eulerian Mixture »
Hypothèses
No particle-particle interaction
No particle effect on fluid flow
9

## Slide 10: 1. CFD one phase liquid validation
Mean velocity
Axial velocity
Validation lines
Mean velocity
Axial velocity
PIV
CFD
10

## Slide 11: 1. Validation of particle size in CFD
Evolution of solid spacial distribution depending on the particle diameter
(color scale +/- 2% [])
+/- 2% []
≥ 95% of Volume
under agitation condition
 Validation of particle diameter
11

## Slide 12: 1. Model validation at different scales
Extrapolation du modèle à 12,5L et 375L
  Ajustement de la vitesse d’agitation
  +/- 2% ≥95% Volume -> Nhs +/- 2,5RPM
Validation expérimentale
  Np = Cste => Transitoire / Turbulent
  Extrapolation de Nhs => Pv = Cste
12
375L
70L
12,5L

## Slide 13: 1. Applications on other geometry / liquid-solid system
Same System on different geometries
Defining placebo to mimic worst solid-liquid vaccines
13

## Slide 14: 2. Simulation of microcarrier suspension for stem cell cultures
2D static culture
CSMs attached on the bottom surface of T=flasks
- Low ratio S/V
- No automation/control
- High operational costs
3D dynamic culture
MSCs attached on microcarriers in suspension in STR
+ High ratio S/V
+ Automation/control possible => How ?
- Quality/Detachment issue (Cell = Product)
- Mechanical stress => Damage to cells ?
?
Context: Improving expansion of stem cells on microcarriers in stirred tank reactors
14

## Slide 15: 2. Simulation of microcarrier suspension for stem cell cultures
Constraints on agitation rate:
No motionless microcarrier at the tank bottom
Low agitation to avoid hydromechanical stresses
⇨ Compromise: N = Njs (complete suspension)
Challenges
Prediction of Njs ?
Zwietering correlation does not predict well Njs for microcarrier suspension
Visual estimation of Njs = Subjective
Spatial distribution of microcarriers ?
Complete suspension
Extensive literature data on glass/sand particles (rS / rL = 2.5) but none on microcarriers (rS / rL ≅ 1)
Context: Improving expansion of stem cells on microcarriers in stirred tank reactors

## Slide 16: 2. Simulation of microcarrier suspension for stem cell cultures
Constraints on agitation rate:
No motionless microcarrier at the tank bottom
Low agitation to avoid hydromechanical stresses
⇨ Compromise: N = Njs (complete suspension)
Context: Improving expansion of stem cells on microcarriers in stirred tank reactors
Challenges
V ≈ 1-10 L
V ≈ 10-100 mL
?
Multiphase CFD ?

## Slide 17: 2. Simulation of microcarrier suspension for stem cell cultures
Numerical method: Choice of the multiphase CFD approach

## Slide 18: 2. Simulation of microcarrier suspension for stem cell cultures
Numerical method: Multiphase CFD approach
HTPG impeller
N = 50 - 200 rpm
V ≈ 1 L
Volume fraction (%) |  | 1 | 2,5 |  | 5 |  | 10
Mesh size (106 cells) |  | 1,5 | 2,1 |  | 3,5 |  | 
Impeller rotation |  | Moving Reference Frame |  |  | Moving Mesh |  | 
Multiphase model |  | Mixture-(Granular) |  |  | Euler-(Granular) |  | 
Turbulence model | Liquid Phase | k-epsilon standard |  |  | other RANS models |  | 
 | Solid Phase | Mixture |  | Dispersed |  | Per Phase | 
Drag function |  | Schiller-Naumann |  |  | Huilin-Gidaspow |  | 
Turbulence interaction models |  | none |  |  | Simonin et al. |  | 
Turbulent dispersion force |  | none |  |  | Simonin et al. |  | 
 |  | 1 | 2,5 |  | 5 |  | 10
Mesh size (106 cells) |  | 1,5 | 2,1 |  | 3,5 |  | 
Impeller rotation |  | Moving Reference Frame |  |  | Moving Mesh |  | 
Multiphase model |  | Mixture-(Granular) |  |  | Euler-(Granular) |  | 
Turbulence model | Liquid Phase | k-epsilon standard |  |  | other RANS models |  | 
 | Solid Phase | Mixture |  | Dispersed |  | Per Phase | 
Drag function |  | Schiller-Naumann |  |  | Huilin-Gidaspow |  | 
Turbulence interaction models |  | none |  |  | Simonin et al. |  | 
Turbulent dispersion force |  | none |  |  | Simonin et al. |  | 
Solid phase:
dP = 170 µm
rS = 1015 kg.m-3
amax= 63 %
Liquid phase:
= 997.5 kg.m-3
= 0.911 mPa.s
(Water at 23°C)
CFD code: ANSYS Fluent R19.2

## Slide 19: 2. Simulation of microcarrier suspension for stem cell cultures
Experimental method: Light attenuation technique
Hemispherical-bottom tank
H = T = 0.12 m (V = 1.12 L)
Probes + Baffles
Backlight LED
Aquarium filled with water
Camera CMOS 4 Mpixels
Axial impeller HTPG
C/T = D/T = 0.5
Material
rS = 1015 kg/m3
dP = 170 µm
Liquid: Phosphate Buffer Saline (PBS) 0.01 M
Cytodex-1 microcarrier
Diameter depends on the salt concentration
Translucent
Solid:

## Slide 20: 2. Simulation of microcarrier suspension for stem cell cultures
Experimental method: Light attenuation technique
Increasing solid volume fraction a
Suspended solid fraction as a function of N
Averaged volume fraction –
Measured vs expected
Increasing impeller speed N (a = 10 %)

## Slide 21: 2. Simulation of microcarrier suspension for stem cell cultures
Results: Solid spatial distribution – Exp. vs CFD
N = 50 rpm
N = 60 rpm
N = 70 rpm
N = 80 rpm
N = 90 rpm
Exp.
CFD

## Slide 22: 2. Simulation of microcarrier suspension for stem cell cultures
Conclusions:
Best CFD modeling approach : Euler-Granular approach with Huilin-Gidaspow drag force model
No influence of the solid phase turbulence model (liquid and solid share the same k and e whatever the model)
No influence of the turbulence interaction model (the solid has no influence on the liquid)
Dramatic influence of the turbulence dispersion force (overprediction of the solid dispersion when used)
Overestimation of Njs with the CFD approach
Strong influence of the mesh refinement at the bottom wall
Potential issues:
Turbulence closure model ?
Small volume and low Njs
Low Reynolds number Re = 3000 – 6000
Low wall-y+
Single-phase PIV
Liquid-solid interaction models ?
Influence of the solid on the liquid ? And vice versa ?
Multiphase turbulence model ?
Liquid solid interaction model ?
Turbulent dispersion force ?
Two-phase PIV

## Slide 23: Conclusions
Thanks !
Any questions ?
23