## Slide 1: Using H2 for CO2 activation on the way towards synthetic fuels
Antoine ROUXHET
European PhD Hydrogen Conference
(EPHyC 2024)
Supervisor: Grégoire Léonard

## Slide 2: The Energy Crisis: a dilemma
Meet the increasing
energy demand
Limit GHG emissions
><
https://ourworldindata.org/grapher/global-primary-energy
Hannah Ritchie, Max Roser and Pablo Rosado (2020) - "CO₂ and Greenhouse Gas Emissions". Published online at OurWorldInData.org. Retrieved from: 'https://ourworldindata.org/co2-and-greenhouse-gas-emissions' [Online Resource]

## Slide 3: A possible solution: the Trias Energetica
Lysen, E H. The Trias Energica: Solar energy strategies for developing countries. Germany: N. p., 1996. Web.

## Slide 4: Implications of the Trias Energetica concept
Variable (time)
  storage required
Variable (location)
  transport required
Large amount of CO2 available

## Slide 5: The power-to-fuel concept
CO2
Air capture
Industries
Renewables
H2O
H2
CO2
H2
Fuels for mobility & industry
Petrochemistry
Energy storage
Residual heat
CO2
2. CO2 capture
1. Water electrolysis
3. Synthesis of hydrocarbons
4. Carbon circularity

## Slide 6: The power-to-fuel concept
CO2
Air capture
Industries
Renewables
H2O
H2
CO2
H2
Fuels for mobility & industry
Petrochemistry
Energy storage
Residual heat
CO2
2. CO2 capture
1. Water electrolysis
3. Synthesis of hydrocarbons
4. Carbon circularity

## Slide 7: From the CO2 molecule to the synthetic fuel…
CO2
H2
Synthetic fuels
C
H
H
n CO2 + (3n+1) H2 ↔ CnH2n+2 + 2n H2O
Reaction difficult to achieve in a single step
  CO2 molecule highly stable
  C-C bonds hard to form
Indirect synthesis of synthetic fuels

## Slide 8: From the CO2 molecule to the synthetic fuel…
CO2
H2
C
H
H
C
O
CO2 + H2 ↔ CO + H2O
reverse water-gas shift reaction (rWGS)
n CO + (2n+1) H2 ↔ CnH2n+2 + n H2O
Fischer-Tropsch reaction

## Slide 9: Objectives of our work
rWGS reaction
Standardisation
Design and optimisation
Dynamic study
rWGS reactor
Fischer-Tropsch reactor
Separation steps
CO2
H2
CO
H2
Hydrocarbons mixture
Kerosene
Gasoline, diesel…
Methanol reactor, ethanol reactor,…
Methanol, ethanol…

## Slide 10: rWGS reaction operating conditions
CO2 + H2 ⇔ CO + H2O ΔH° = +41 kJ/mol
CO2 + 4 H2 ⇔ CH4 + 2 H2O ΔH° = -165 kJ/mol
CO + 3 H2 ⇔ CH4 + H2O ΔH° = -206 kJ/mol
+ exothermic solid carbon formation
T° ≈ 800 – 900°C
P ≈ 1 – 30 bar
A. Rouxhet, M. E. A. Berchiche, and G. Léonard, “A Review of the Reverse Water-Gas Shift Reaction as an Intermediate Step in Power-to-Fuels Processes.” unpublished.

## Slide 11: rWGS reactor at equilibrium – conditions influence
Chart: Temperature (°C)
| 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000
CO2 | 0.25003 | 0.25051 | 0.25318 | 0.2584 | 0.24929 | 0.19422 | 0.13994 | 0.11594 | 0.099955 | 0.087621
H2 | 0.00022507 | 0.0041127 | 0.027936 | 0.10258 | 0.24008 | 0.39259 | 0.45696 | 0.44805 | 0.43316 | 0.42094
CO | 3.0217e-08 | 8.7158e-06 | 0.00035845 | 0.005052 | 0.03511 | 0.11983 | 0.19106 | 0.21721 | 0.23336 | 0.24571
H2O | 0.49983 | 0.49692 | 0.47914 | 0.42433 | 0.32872 | 0.23552 | 0.20505 | 0.21827 | 0.23347 | 0.24573
CH4 | 0.24992 | 0.24845 | 0.23939 | 0.20964 | 0.14681 | 0.057841 | 0.0069928 | 0.00052594 | 5.5112e-05 | 8.1745e-06
P = 1 bar --- Inlet H2/CO2 = 2
CH4 production limited above 700°C at 1 bar

## Slide 12: rWGS reactor at equilibrium – conditions influence
Chart: Temperature (°C)
| 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000
CO2 | 0.25 | 0.25008 | 0.25056 | 0.25174 | 0.2517 | 0.24203 | 0.21005 | 0.15893 | 0.11459 | 0.090764
H2 | 3.25e-05 | 0.00067359 | 0.0049271 | 0.020098 | 0.056218 | 0.12033 | 0.21048 | 0.30987 | 0.38343 | 0.40898
CO | 5.555e-09 | 1.5912e-06 | 6.4434e-05 | 0.00087722 | 0.0060882 | 0.026294 | 0.075722 | 0.14835 | 0.20953 | 0.24041
H2O | 0.49998 | 0.4995 | 0.49632 | 0.48515 | 0.45936 | 0.41633 | 0.36107 | 0.30469 | 0.26481 | 0.25337
CH4 | 0.24999 | 0.24975 | 0.24813 | 0.24213 | 0.22664 | 0.19502 | 0.14268 | 0.07817 | 0.02764 | 0.0064796
P = 30 bar --- Inlet H2/CO2 = 2
H2
H2O
CO
CO2
CH4

## Slide 13: rWGS reactor at equilibrium – conditions influence
Chart: Temperature (°C)
| 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000
P = 1 bar w/o C | 0.49989 | 0.49795 | 0.48637 | 0.45378 | 0.42187 | 0.47777 | 0.58599 | 0.65255 | 0.70018 | 0.73715
P = 30 bar w/o C | 0.49998 | 0.49967 | 0.49763 | 0.49117 | 0.48041 | 0.47764 | 0.50974 | 0.58767 | 0.67423 | 0.73119
P = 30 bar
P = 1 bar
Constant inlet H2/CO2 = 2
Chart: Temperature (°C)
| 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000
P = 1 bar w/o C | 1.2094e-07 | 3.5086e-05 | 0.0014954 | 0.023537 | 0.19303 | 0.67447 | 0.96469 | 0.99758 | 0.99976 | 0.99997
P = 30 bar w/o C | 2.2221e-08 | 6.3712e-06 | 0.00025961 | 0.0036098 | 0.026161 | 0.11881 | 0.34672 | 0.6549 | 0.88346 | 0.97375
P = 1 bar
P = 30 bar
CO2 conversion and CO selectivity favoured at low pressure

## Slide 14: rWGS reactor at equilibrium – conditions influence
Chart: Temperature (°C)
| 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000
P = 1 bar w/o C | 0.49989 | 0.49795 | 0.48637 | 0.45378 | 0.42187 | 0.47777 | 0.58599 | 0.65255 | 0.70018 | 0.73715
P = 1 bar w/ C | 0.76404 | 0.66278 | 0.58563 | 0.51704 | 0.45716 | 0.47777 | 0.58599 | 0.65255 | 0.70018 | 0.73715
P = 30 bar w/o C | 0.49998 | 0.49967 | 0.49763 | 0.49117 | 0.48041 | 0.47764 | 0.50974 | 0.58767 | 0.67423 | 0.73119
P = 30 bar w/ C | 0.81955 | 0.6954 | 0.61247 | 0.55403 | 0.51069 | 0.48396 | 0.50974 | 0.58767 | 0.67423 | 0.73119
P = 30 bar
P = 1 bar
Constant inlet H2/CO2 = 2
Chart: Temperature (°C)
| 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000
P = 1 bar w/o C | 1.2094e-07 | 3.5086e-05 | 0.0014954 | 0.023537 | 0.19303 | 0.67447 | 0.96469 | 0.99758 | 0.99976 | 0.99997
P = 1 bar w/ C | 3.0186e-08 | 1.5325e-05 | 0.00090871 | 0.016891 | 0.15556 | 0.67447 | 0.96469 | 0.99758 | 0.99976 | 0.99997
P = 30 bar w/o C | 2.2221e-08 | 6.3712e-06 | 0.00025961 | 0.0036098 | 0.026161 | 0.11881 | 0.34672 | 0.6549 | 0.88346 | 0.97375
P = 30 bar w/ C | 3.7266e-09 | 2.3519e-06 | 0.00014636 | 0.0026345 | 0.022394 | 0.11478 | 0.34672 | 0.6549 | 0.88346 | 0.97375
P = 1 bar
P = 30 bar
Coking reaction only impacts CO2 conversion at low temperature

## Slide 15: Major perspective: a pilot-scale installation

## Slide 16: Major perspective: a pilot-scale installation
H2 source = water electrolysis max. 1.5 Nm³/h

## Slide 17: Take-home messages
In the future, increasing need to store and transport energy
  Power-to-fuel concept offers a solution
  Fuels present high energy density per unit volume
Indirect synthesis from captured CO2 and H2
  rWGS pathway = CO2 activation by transformation into CO
High temperature required to limit CH4 production
Optimal pressure not as straightforward
Pilot installation converting CO2 to kerosene soon at ULiège

## Slide 18
Thank you for your attention!
Antoine ROUXHET
This papper is supported by the Walloon Region as part of a FRIA grant (F.R.S.-FNRS).