## Slide 1
Improving taste and flavor in dairy products through milk analysis of free fatty by Mid-infrared (MIR) spectrometry
Octave CHRISTOPHEa,b, Romain Redingc, Julie LEBLOISd Denis Pittoise, Cédric Grignarde and Frédéric DEHARENGa
aWalloon Agricultural Research Center (CRA-W) Belgium bUniversity of Liège, Gembloux Agro-Bio Tech, Belgium cCONVIS, 9084 Ettelbruck, Luxembourg dElevéo asbl, AWE groupe 5590 Ciney, Belgium eLuxembourg Institute of Science and Technology (LIST), Luxembourg
??
Lipase
Free Fatty Acids (FFA)
Glycerol
Triglycerides
The dairy sector deals with a recurring issue: a defect of taste appearing due to degradation of fat, commonly called lipolysis.
Lipolysis happens after the milking, through the physical shocks induced by freezing, pumping, transfer and storage of the milk. Physical break of fat globules makes triglycerides accessible to enzymes and degraded into free fatty acids (FFA).
Among them, the volatile short chain FFA lead to organoleptic issues through undesired tastes.
Introduction
Lipolysis why it’s bad ?  Cause bad taste of the milk
Butyric acid (C4:0)
Rancid taste
Caproic acid (C6:0)
Caprylic acid (C8:0)
Capric acid (C10:0)
Rancid taste
Other FFA (C12:0  C18:3)  effect on milk transformation + Inhibition of bacteria
Results
20% of the samples were above the limit of quantification (LOQ).
A protocol for inducing lipolysis is therefore needed to create models for quantifying FFAs.
Homogenisation of the sample  strong lipolysis over time + compatible with Mid infrared spectroscopy.
Decreasing the diameter of fat globules
Destruction of milk fat membrane
 Triglycerides more
available to lipolysis
Milk Fat globule
a)Quantification
792 samples analysed  GCMS/MS to obtain the FFA values.
Models were built for free fatty acid using several algorithms: Principal Component Regression (PCR), Partial Least Square regression (PLSr), Elasticnet regression, Kernel Ridge regression (KRR) and Support Vector Machine-Regression (SVM-R)
A cross validation 10 groups subset and random external validation with 20% of total sample  evaluate models
FFA | Algo | R²cal | R²cv | R²val | RMSEcal | RMSEcv | RMSEval | RPDcal | RPDcv | RPDval
C4 | KRR | 0.85 | 0.73 | 0.76 | 14.79 | 19.85 | 16.75 | 2.58 | 1.92 | 2.28
C6 | ElasticNet | 0.77 | 0.68 | 0.57 | 9.74 | 11.58 | 12.70 | 2.10 | 1.77 | 1.61
C8 | SVM-R | 0.85 | 0.54 | 0.40 | 4.95 | 8.71 | 9.72 | 2.61 | 1.48 | 1.33
C10 | KRR | 0.59 | 0.52 | 0.38 | 8.88 | 9.62 | 9.15 | 1.56 | 1.44 | 1.51
C12 | PCR | 0.35 | 0.31 | 0.08 | 6.45 | 6.65 | 6.34 | 1.24 | 1.21 | 1.26
C14 | KRR | 0.52 | 0.40 | 0.02 | 9.91 | 11.06 | 11.04 | 1.44 | 1.29 | 1.29
C16 | KRR | 0.50 | 0.36 | 0.20 | 22.40 | 25.25 | 21.82 | 1.41 | 1.25 | 1.45
C18 | PLS | 0.70 | 0.59 | 0.49 | 11.18 | 12.99 | 12.48 | 1.81 | 1.56 | 1.62
b)Modelling
Table 1: Modelling performances of each Free Fatty acid with the best algorithm based on lowest RMSE from the external validation
Figure 1: Graphical representation of the lipolysis of triglycerides into Free Fatty Acid in milk
Figure 2: Illustration of the homogenization of milk fat globule
Figure 2: C4 model including spontaneous lipolysis and
homogenized sample with kernel Ridge Regression
Conclusion: This work presents encouraging performances of Free Fatty acid prediction and exhibit the potential to detect specific milk flavor issues.
Acknowledgement:
o.christophe@cra.wallonie.be
LinkedIn