## Slide 1: Comparative Assessment of Fuel-Switching Options for the Energy Transition in the Cement Industry
Muhammad Salmana, Daniel Flórez-Orregob,François Maréchalb, Grégoire Léonarda
aChemical Engineering, University of Liège, Belgium.
bIPESE group, Federal Polytechnic School of Lausanne, Sion, Switzerland.

## Slide 2: Contents
Introduction
Methodology
Key results
Conclusion
Next steps
Salman et al.

## Slide 3
Salman et al.
https://www.globalcement.com/news/item/17601-italian-cement-association-federbeton-warns-against-cement-production-moving-out-of-eu

## Slide 4: Introduction
Why Cement?
  A hard-to-abate sector, central to infrastructure and development
  Responsible for ~7–8% of global CO₂ emissions
  Emissions arise from both:
    Calcination (process emissions from limestone decomposition)
    Fossil fuel combustion (heat for kilns)
What Are the Key Challenges?
  Highly energy- and carbon-intensive process
  EU ETS price increases can impact competitiveness
  Risk of industrial relocation (carbon leakage & deindustrialisation)
What Do We Need to Do?
  Conduct a systematic evaluation of all decarbonisation levers
  Identify cost-effective and low-risk pathways
Salman et al.

## Slide 5
Cement Production Process
Salman et al.
https://www.catf.us/resource/role-carbon-capture-storage-decarbonising-europes-cement-sector/

## Slide 6
Salman et al.

## Slide 7: Decarbonization of the Cement Industry: A Comprehensive Techno-Economic Assessment of Low-Emission Pathways
Techno-economic comparison of decarbonisation options
Ranking of options based on future energy scenarios
Mapping of options based on multiple variables
Salman et al.

## Slide 8: Methodology
Decarbonization of the Cement Industry

## Slide 9
Methodology for superstructure optimization
Salman et al.

## Slide 10: Cement Superstructure
Typical European cement plant with 5000 tonnes of clinker production per day
Superstructure of Decarbonisation
options for Cement Industry
Salman et al.

## Slide 11
Kiln Options
Conventional Kiln
Oxy-combustion kiln
Plasma kiln
Hybrid-Plasma Kiln
Salman et al.

## Slide 12: Conventional Kiln – Fuel/Air
Voldsund, M. et al. (2019). Comparison of technologies for CO₂ capture from cement production—Part 1: Technical evaluation. Energies, 12(3), 559
Salman et al.

## Slide 13: Oxycombustion kiln with CPU
Salman et al.
Voldsund, M. et al. (2019). Comparison of technologies for CO₂ capture from cement production—Part 1: Technical evaluation. Energies, 12(3), 559

## Slide 14: Electrification
Complete Electrification
Partial Electrification (Hybrid)
Salman et al.
Quevedo Parra, S., & Romano, M. C. (2025). Decarbonization of cement production by electrification. Journal of Cleaner Production

## Slide 15
Carbon Capture Options
MEA-based Chemical Absorption Process
Oxy-combustion with CO2 compression and purification unit (CPU)
Calcium Looping
Salman et al.

## Slide 16: MEA Chemical Absorption Process
MEA
Salman, M. et al. (2024). Techno-economic analysis of AMP/PZ solvent for CO₂ capture in a biomass CHP plant: Towards net negative emissions. Frontiers in Energy Research, 12.
Salman et al.

## Slide 17: CO2 compression and Purification Unit - CPU
Shah, M.M., 2011. 11 - Carbon dioxide (CO2) compression and purification technology for oxy-fuel combustion, in: Zheng, L. (Ed.), Oxy-Fuel Combustion for Power Generation and Carbon Dioxide (CO2) Capture. Woodhead Publishing, pp. 228–255.
Salman et al.

## Slide 18: CaL Process
Salman et al.

## Slide 19
Waste Heat Recovery
Supercritical CO2 Rankine Cycle
Heat recovered for Carbon Capture
Salman et al.

## Slide 20
Supercritical CO2
Rankine Cycle
Salman et al.

## Slide 21: Blueprint
Equation-oriented Lua script models
Includes detailed mass and energy profile of a process/unit.
Costing details (CAPEX and OPEX)
Emissions data (Scope 1 and 2)
It consists of several elements:
  Units: elementary black box ‘node’ of the system.
  Streams
  Parameters: used in the streams and units to define size, cost, T, P etc.,)
It can be associated with a predefine simulation model (e.g. Aspen model)
Salman et al.

## Slide 22: OSMOSE tool by IPESE group of EPFL
A framework for process and energy systems optimisation
Simultaneous optimisation of thermodynamic, environmental, and economic elements.
A decision support tool
Coupled with databases, simulation tools, optimisation methods, solvers and post-analysis methods.
Incorporate a database of Blueprints (equation-oriented LUA) models
Utilise AMPL language to solve MILP problems
Blueprint Models
OSMOSE
Optimization results
Salman et al.

## Slide 23: Objective Function
Total emissions impact (TEI) … (Direct + Indirect emissions)
Energy balance and
feasibility constraints
Salman et al.

## Slide 24: Configurations
Fuel switching
Coal-fired kiln (base case)
NG-fired kiln
Biogas-fired kiln
H2/NG co-firing (50% share)
Biomass Co-firing (50% share)
Municipal solid waste Co-firing (50% share)
Electrification
Partial Electrification: Plasma pre-calciner + Biomass oxy-fired kiln + CPU
Full Electrification:
  (Plasma pre-calciner + Plasma kiln + CPU)
Capture Options
MEA Chemical Absorption
Oxy-firing with cryogenic capture
Calcium Looping
Storage Options
Injection in depleted fields
Waste heat recovery
For Carbon Capture, Power generation or District heating
Salman et al.
Notes: MSW: C(47.1%), H(5.1%), O(30.9%), N(1.6%). S(0.8%), Cl(0.7%) – dry ash-free basis
BM: Ultimate analysis (mass basis): 47%C, 6%H, 45%O, 0%N, 0%S

## Slide 25
No. | Configuration | Abbreviation
1 | Coal fired kiln | Coal
2 | Coal-fired kiln with MEA carbon capture | Coal_CC
3 | Coal-oxy-fired kiln with cryogenic capture | Coal_oxy_CC
4 | Coal-fired kiln with CaL capture | Coal_CaL
5 | Natural Gas fired kiln | NG
6 | Natural Gas-fired kiln with MEA carbon capture | NG_CC
7 | Natural Gas-oxy-fired kiln with cryogenic capture | NG_oxy_CC
8 | Natural Gas-fired kiln with CaL capture | NG_CaL
9 | Biomethane fired kiln | BioCH4
10 | Biomethane-fired kiln with MEA carbon capture | BioCH4_CC
11 | Biomethane-oxy-fired kiln with cryogenic capture | BioCH4_oxy_CC
12 | Biomethane-fired kiln with CaL capture | BioCH4_CaL
13 | Biomass co-firing kiln | BM
14 | Biomass-fired kiln with MEA carbon capture | BM_CC
15 | Biomass-oxy-fired kiln with cryogenic capture | BM_oxy_CC
16 | Biomass-fired kiln with CaL capture | BM_CaL
17 | Municipal waste co-firing kiln | MSW
18 | Municipal waste co-firing kiln with MEA carbon capture | MSW_CC
19 | Municipal waste oxy-co-firing kiln with cryogenic capture | MSW_oxy_CC
20 | Municipal waste co-firing kiln with CaL capture | MSW_CaL
21 | Hydrogen co-firing kiln | H2
22 | Hydrogen kiln with MEA carbon capture | H2_CC
23 | Hydrogen-oxy kiln with cryogenic capture | H2_oxy_CC
24 | Hydrogen kiln with CaL capture | H2_CaL
25 | Plasma Pre-calciner + Plasma kiln with cryogenic capture | Plasma
26 | Plasma Pre-calciner + Biomass-oxy kiln with cryogenic capture (hybrid kiln) | Hybrid

## Slide 26: Techno-Economic Analysis
Decarbonization of the Cement Industry

## Slide 27: Model Validation – Base-case
Base-case: Air-fired dry kiln (4-stage cyclone preheater pre-calciner) (No CCS)
Waste Heat = From preheater exhaust (300 – 400 °C) + clinker cooling (200 – 300 °C)
Value | Blueprint Model | Industry (Confidential)
Clinker Capacity (tpd) | 5000 tpd | -
Fuel | Coal | -
Solids mass raw material | 1.9 t/t | In range
Fuel consumption | 0.12 t/tclinker | In range
Fuel consumption | 3.48 GJ/tclinker | In range
Emissions (Combustion + Process) | 0.8 tCO2/tclinker | In range
Electricity Consumption | 0.40 GJ/tclinker | In range
Electricity Produced with ORC | 6 MW | In range
Air preheating | 1000 °C | Correct
Raw material preheating | 900 °C | Correct
Exhaust gases after PH and PC | 250 °C | In range
Fuel Consumption Co-firing biomass (50%) | 3.98 GJ/tclinker | In range
Salman et al.

## Slide 28
Energy Consumption Analysis (GJ/t of clinker)
Base
Case
Amine-based
Capture
Oxyfuel-Cryo
Capture
Biomass
Co-firing
kiln
Biomass-CC
BiomassOxy
Electrification
(Plasma)
Hybrid
Calcium
Looping
Hydrogen

## Slide 29
Energy Consumption Analysis (GJ/t of clinker)

## Slide 30: CAPEX Assumptions
Modeled Plant Capacity = 5000 tpd of clinker
Lifetime = 40 years
Discount rate for combustion-based kiln = 6%
Discount rate for plasma-based kiln = 8%
Abbreviations:
  NG: Natural Gas
  BioCH4 = Bio-methane
  BM: Biomass/coal co-firing
  MSW: Municipal Solid Waste co-firing
  H2: Hydrogen
  CCUnit: Chemical absorption-based carbon capture
  Cryocap: cryogenic CO2 purification unit (CPU)
Salman et al.

## Slide 31
Annual CAPEX for each configuration (Million €/year)
Salman et al.

## Slide 32: Scenarios – inspired from (Vito + IEA + ENTSO)
Salman et al.
Price | 2025 | 2040 | 2050
Electricity (€/MWh) | 100 | 65 | 30
Biomethane (€/MWh) | 70 | 45 | 45
Natural Gas (€/MWh) | 35 | 35 | 35
Coal (€/MWh) | 13 | 12 | 12
Biomass (€/MWh) | 16.9 | 18 | 18
MSW (€/MWh) | 5 | 5 | 5
Hydrogen (€/MWh) | 120 | 85 | 55
CO2 (€/tCO2) | 80 | 140 | 200
CO2 T&S (€/tCO2) | 60 | 40 | 20
Electricity Impact (tCO2/MWh) | 0.14 | 0.06 | 0.057
Hydrogen Impact (tCO2/MWh) | 0.357 | 0.28 | 0.18

## Slide 33: Operating Cost (M€/year)
Scenario 2040
Scenario 2025
Salman et al.
Scenario 2050

## Slide 34: Total Annual Cost Comparison
Total Annual
Cost Comparison

## Slide 35: Total Annual Cost Comparison
Salman et al.

## Slide 36: Total Annual Cost Comparison
Salman et al.

## Slide 37: Conclusion
Decarbonization of the Cement Industry

## Slide 38: Conclusions
Waste Heat Recovery (for power generation or CCS) has limited potential.
CCS increases CAPEX, but:
  Cryogenic capture adds only +27% annual CAPEX over the base case.
  Amine-based capture adds around +50% annual CAPEX.
OPEX is mainly driven by ETS price and fuel/electricity cost across all configurations.
In the 2025 scenario:
  Co-firing with biomass or MSW is the most cost-effective.
  CCS options offer deep emission cuts but remain costly.
  Electrification and biomethane + CCS are the most expensive pathways.
By 2040–2050, CCS becomes cost-competitive, with cryogenic capture emerging as the cheapest solution.
Alternative fuels (MSW, Biomass) already provide clear benefits, and increasing their substitution rate offers additional emissions reductions in future scenarios.
Without a higher ETS price, CCS remains cost-intensive. However, cryogenic capture provides a low-cost per ton clinker option and becomes economically viable with only a modest ETS increase.
CaL remains the most expensive CC option.
Salman et al.

## Slide 39: Multi-Scenario Technology Mapping
Future Task

## Slide 40
How to free yourself as an academic from “predicting” prices and not trigger people???
Salman et al.

## Slide 41: Multi-scenario analysis
Independent Variables
Electricity: 10 – 200 €/MWh
Hydrogen: 10 – 200 €/MWh
Natural Gas: 10 – 100 €/MWh
Biomass: 10 – 100 €/MWh
Biogas 10 – 100 €/MWh
Coal: 10 – 100 €/MWh
MSW: 10 – 100 €/MWh
CO2 emissions: 75 – 250 €/tCO2
CO2 T&S: 20 – 100 €/tCO2
Approx. 1,000,000+ Simulations
Salman et al.

## Slide 42: Technology Mapping via Parallel Coordinates

## Slide 43: NGOxy fired furnace
Salman et al.

## Slide 44
Mapping of an energy scenario

## Slide 45
Indecate.com

## Slide 47: Thanks for your attention! Muhammad Salman Daniel Flórez-Orrego François Maréchal Grégoire Léonard Contact: Email: m.salman@uliege.be Tel: +32-465671822