## Slide 1: Refractive index RI matching for PIV measurements of liquid-solid flow in a stirred tank bioreactor used for mesenchymal stem cell culture
Mohamad MADANI, Angélique DELAFOSSE, Dominique TOYE
m.madani@uliege.be Product, Environment, and Processes (PEPs) Department of Chemical Engineering Université de Liège http://chemeng.ulg.ac.be/

## Slide 2: Overview
In vitro expansion
Study on the design and operation of stirred tank bioreactor
Wide applications in medicine:
Gene therapy
Bone reconstruction
Repairing damaged tissues
Due to:
Differentiation & immunosuppressive properties
Insufficient quantities (<106 cells per sample)
Why?
Desired:107 to 109 cells per injected dose
Overview
Problematic
Materials and Methods
Results
Prospects
Notes: Higher doses

## Slide 3: Principle
Increasing rotation speed N
Overview
Problematic
Materials and Methods
Results
Prospects
Cells are anchorage dependent: adherence on particles to expand, e.g., commercial Cytodex-1
Suspending microcarriers to ensure nutrient transfer and mixing
Increase in agitation → more suspension → higher stresses and collisions → higher cells detachment and death
Unique system: ρL/ρS ≈1 and low viscosity
2-3 v% of microcarriers
characterizing hydrodynamics:  Relative velocities
 Turbulence
 Solids interactions
Notes: Not so often studied in literature

## Slide 4: Reactor configuration
HTPGD: axial 3-blade impeller – down pumping
V = 0.7 L
T = 0.12 m
H = 0.082 m
C/T = D/T = 0.5
T: tank diameter (m)
C: off-bottom impeller clearance (m)
D: impeller diameter
H: liquid height or depth (m)
HTPG impeller by: www.pierreguerin.com
Overview
Problematic
Materials and Methods
Results
Prospects
Solids loading

## Slide 5: PIV – Particle Image Velocimetry
Laser
Pulse YAG 2x65mJ/532nm
CMOS camera
FlowSense EO 4M, 16-25 Hz
Aquarium filled with paraffine oil
Stirred tank
Previous test
Cytodex-1 microcarrier in water
rS = 1020 kg/m3
dP = 170 µm
Overview
Problematic
Materials and Methods
Results
Prospects
Notes: Seems Translucent

## Slide 6: Problematic – PIV
αs = 0.5 %v!
PIV raw image
Cytodex-1/water seeded with: Rhodamine (1-10 µm)
αs = 0.5 %v only!
Blurry results, insufficient for retrieving data
Issue:
poor optical characteristics for cytodex-1/water system
Light scattering!
Alternative solid/liquid model with good optical properties to evaluate velocities and fluctuations
Overview
Problematic
Materials and Methods
Results
Prospects
Notes: matched RI, density and viscosity

## Slide 7: Matched RI for PIV
Microparticles
+
Matched density system
Additional limitations:
RI matched
Chemical compatibility
Safety concerns
Water absorption of particles
Low viscosity ranges
Theoretically
PMMA particles/AMMONIUM THIOCYANATE NH4SCN
CYTODEX-1/WATER
Reference: Borerro et al 2016
Overview
Problematic
Materials and Methods
Results
Prospects
Notes: Single particle properties Flow regime Estimated dissipated energy Stokes number

## Slide 8: PMMA/NH4SCN characterization
PMMA/NH4SCN
Compatibility evaluation via Microscope
Properties | PMMA/NH4SCN | Cytodex-1/Water
ρL/ρS (-) | ≈0.96 | ≈0.97
μL mPa.s | ≈1.5-1.9 | ≈1
Particles size dS μm | ≈168 | ≈170
Terminal velocity 10-4 m/s | ≈5-6 | ≈2.4
Njs ±3 rpm for αs ≈ 2.5 %v | ≈108 | ≈77
NH4SCN Solution of 55-61 wt%, T= 21-23°C
same ranges of Reynolds number (Re = 5000-6000)
Stokes number is retained
RI≈1.486-1.491
Overview
Problematic
Materials and Methods
Results
Prospects

## Slide 9: PIV – multiphase
Evaluation of liquid phase
- Solid phase: PMMA microparticles
- Spatial resolution: ≈1.16 mm
- Frequency: 16 Hz
- Number of images: 1000
- Full Homogeneous suspension N=150 rpm
61 wt% NH4SCN - ρL= 1139 kg.m-3
seeded with Rhodamine coated PMMA (1-20 µm)
- Liquid phase:
Overview
Problematic
Materials and Methods
Results
Prospects
Experimental error: 3-8%

## Slide 10: PIV – raw images
αs= 0 v % (blank)
αs= 3 v %
Overview
Problematic
Materials and Methods
Results
Prospects

## Slide 11: Contour plot
Mean flow magnitude
Turbulent kinetic energy TKE
Overview
Problematic
Materials and Methods
Results
Prospects
R mm
R mm
r/R =0.51
r/R =0.9

## Slide 12: Profile plot
Mean flow
In front of the blade
No significant impact
Far from the blade, near the wall
9% difference at the peak
Overview
Problematic
Materials and Methods
Results
Prospects

## Slide 13: Profile plot
Turbulent kinetic energy TKE
In front of the blade
Far from the blade, near the wall
20% difference at the peak
17.3% difference at the peak
Induce in turbulence
Overview
Problematic
Materials and Methods
Results
Prospects

## Slide 14: Average Absolute Shear rate
Overview
Problematic
Materials and Methods
Results
Prospects
R mm

## Slide 15: Average Absolute Shear rate
Statistical distribution
In presence of solids:
Shift to higher shear rates
Higher fractions persist at high shear values
Overview
Problematic
Materials and Methods
Results
Prospects
Notes: To understand the effect more, different percentile plots are examined

## Slide 16: Average Absolute Shear rate
10% increase
Global average of shear rate in the domain
Overview
Problematic
Materials and Methods
Results
Prospects
Percentiles of average shear rate

## Slide 17: Conclusions
A shift in liquid-solid system based on RI matching was necessary, while preserving initial system properties (cytodex/water) for a compatible analysis
PIV tests conducted for the new model on the liquid phase: alteration in turbulence
Useful data for CFD modeling
Next: PIV measurements on the solid phase  Relative velocities
Camera 1
Camera 2
Overview
Problematic
Materials and Methods
Results
Prospects
Notes: Focus more on PIV

## Slide 18: Thanks for your attention!
The authors are grateful to the FNRS for their financial support.
m.madani@uliege.be

## Slide 19: Turbulence Modulations
Parameter | description | Criteria
Particle diameter to integral length scale Gore and Crowe (1991) | dp/le | dp/le <0.1: Turbulence attenuation dp/le >0.1: Turbulence augmentation
particle stokes number - Elghobashi (1994) | St=τp/τη | St<1: particles follow fluid streamlines St>1: poor particle response to flow
Particle Reynolds number - Hetsroni (1989) | Rep =(uf – up)dp/ | Rep <100: turbulence attenuation Rep >400: turbulence augmentation
Particle momentum number Tanaka and Eaton (2008) | Pa = StRe2(η/L)3 | 3x103  Pa  105: turbulence attenuation Pa<3x103, Pa>105: turbulence augmentation
dp/le = 0.023<0.1
Pa = 0.03< 3x103
St = 0.078
Contradicting
In agreement

## Slide 20: For αs= 3 v % At Njs =114 rpm
Profile plot near the wall at r/R =0.9

## Slide 21: CFD Test – cytodex-1/water
HTPG impeller
N = 50 - 200 rpm
V ≈ 1 L
Volume fraction (%) |  | 1 | 2,5 |  | 5 |  | 10
Mesh size (106 cells) |  | 1,5 | 2,1 |  | 3,5 |  | 
Impeller rotation |  | Moving Reference Frame |  |  | Moving Mesh |  | 
Multiphase model |  | Mixture-(Granular) |  |  | Euler-(Granular) |  | 
Turbulence model | Liquid Phase | k-epsilon standard |  |  | other RANS models |  | 
 | Solid Phase | Mixture |  | Dispersed |  | Per Phase | 
Drag function |  | Schiller-Naumann |  |  | Huilin-Gidaspow |  | 
Turbulence interaction models |  | none |  |  | Simonin et al. |  | 
Turbulent dispersion force |  | none |  |  | Simonin et al. |  | 
 |  | 1 | 2,5 |  | 5 |  | 10
Mesh size (106 cells) |  | 1,5 | 2,1 |  | 3,5 |  | 
Impeller rotation |  | Moving Reference Frame |  |  | Moving Mesh |  | 
Multiphase model |  | Mixture-(Granular) |  |  | Euler-(Granular) |  | 
Turbulence model | Liquid Phase | k-epsilon standard |  |  | other RANS models |  | 
 | Solid Phase | Mixture |  | Dispersed |  | Per Phase | 
Drag function |  | Schiller-Naumann |  |  | Huilin-Gidaspow |  | 
Turbulence interaction models |  | none |  |  | Simonin et al. |  | 
Turbulent dispersion force |  | none |  |  | Simonin et al. |  | 
Solid phase:
dP = 170 µm
rS = 1015 kg.m-3
amax= 63 %
Liquid phase:
= 997.5 kg.m-3
= 0.911 mPa.s
(Water at 23°C)
CFD code: ANSYS Fluent R19.2

## Slide 22: CFD Test
Liquid flow in presence of a solid phase (N = 200 rpm): TKE
Not fully evaluated
No clear influence of the solid phase on the liquid phase